## Slide 1: Fall Protection Systems II
Fall Prevention in Construction
Criteria and Practices

## Slide 2: Learning Objectives 1
Understanding the basic and best practices associated with the following Fall Protection Systems:
    Positioning Devices
    Fall Restraint
    Warning Lines
    Controlled Access Zones
Fall Protection Systems II

## Slide 3: Learning Objectives 2
Understanding the basic and best practices associated with the following Fall Protection Systems:
    Safety Monitor Systems
    Covers
    Protection from Falling Objects
    Fall Protection Plan
    Fall Protection Training Requirements
Fall Protection Systems II

## Slide 4: Basic Question 1
How many feet from an unprotected edge constitutes as fall protection?
    Meaning how far away from a fall hazard is far enough that you don’t need a protective system?
Fall Protection Systems II

## Slide 5: Basic Question 2
There is no safe distance from any unprotected edge
How many feet from an unprotected edge constitutes as fall protection?
    Meaning how far away from a fall hazard is far enough that you don’t need a protective system?
Fall Protection Systems II

## Slide 6: Positioning Device Systems
OSHA defines a positioning device system as a body belt or body harness system rigged to allow a worker to be supported on an elevated vertical surface, such as a wall, and work with both hands free while leaning.
Body belt or body harness systems are to be set up so that a worker can free fall no farther than 2 feet.
    BEST PRACTICE IS STOP USING BODY BELTS!
Body belts or harnesses must be secured to an anchorage capable of supporting at least twice the potential impact load of a worker’s fall or 3,000 pounds, whichever is greater.
Fall Protection Systems II
Notes: 1926.502(e)(2)Positioning devices shall be secured to an anchorage capable of supporting at least twice the potential impact load of an employee's fall or 3,000 pounds (13.3 kN), whichever is greater.

## Slide 7: Fall Restraint Systems 1
While fall restraint systems are not mentioned in Subpart M, OSHA recognizes a fall restraint system as a means of prevention. The system, if properly used, tethers a worker in a manner that will not allow a fall of any distance.
    This system is comprised of a body belt or body harness, an anchorage, connectors, and other necessary equipment. Other components typically include a lanyard, a lifeline, and other devices.
    For a restraint system to work, the anchorage must be strong enough to prevent the worker from moving past the point where the system is fully extended, including an appropriate safety factor.
Fall Protection Systems II
Notes: 1926.502(d)"Personal fall arrest systems." Personal fall arrest systems and their use shall comply with the provisions set forth below. Effective January 1, 1998, body belts are not acceptable as part of a personal fall arrest system. Note: The use of a body belt in a positioning device system is acceptable and is regulated under paragraph (e) of this section.

## Slide 8: Fall Restraint Systems 2
Fall restraint assumes the employee cannot reach the edge.
He is basically on a short leash.
If the employee could reach to the edge and fall over the edge, he must be in fall arrest.
1910.140(b) and ANSI/ASSP Z359.15-2014 Safety Requirements for Single Anchor Lifelines and Fall Arresters for Personal Fall Arrest Systems
Fall Protection Systems II

## Slide 9: Warning Line Systems 1
OSHA defines a warning line system as a barrier erected on a roof to warn workers that they are approaching an unprotected roof side or edge, and to designate an area in which roofing work may take place without the use of guardrails, body harnesses, or safety net systems to protect workers in the area.
    Warning line systems consist of ropes, wires, or chains, plus supporting stanchions.
Fall Protection Systems II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 10: Warning Line Systems 2
The warning line must be erected around all sides of roof work areas.
When mechanical equipment is not being used, the warning line must be erected at least 6 feet from the roof edge.
When mechanical equipment is being used the warning line must be erected:
    At least 6 feet from the roof edge parallel to the direction of mechanical equipment operation; and
    At least 10 feet from the roof edge perpendicular to the direction of mechanical equipment operation.
Fall Protection Systems II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 11: Warning Line Systems 3
Warning lines must be established before work begins.
All workers must be trained. 1926.503(a)(2)
No work outside warning lines without fall protection. 1926.502(f)(3)
May be used on flat and low slope roofs. 1926.501(b)(10)
Safety monitoring should be used sparingly.
Employees must comply promptly with warnings and directions. 1926.502(h)(4)
Fall Protection Systems II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 12: Warning Line Systems 4
The rope, wire, or chain must be flagged at not more than 6-foot intervals with high-visibility material and have a minimum tensile strength of 500 pounds.
The rope, wire, or chain must be rigged and supported so that:
    The lowest point (including sag) is at least 34 inches from the walking or working surface; and
    Its highest point is no more than 39 inches from the walking or working surface.
    Pulling on one section of the line between stanchions will not result in slack being taken up in the adjacent section before the stanchion tips over.
Stanchions, after being rigged with warning lines, must be capable of resisting, without tipping over, a force of at least 16 pounds applied horizontally against the stanchion, 30 inches above the walking or working surface, perpendicular to the warning line and in the direction of the floor, roof, or platform edge.
1926.502(f)(2)
Fall Protection Systems II
Notes: 1926.502(f)"Warning line systems." Warning line systems [See 1926.501(b)(10)] and their use shall comply with the following provisions:
1926.502(f)(1)The warning line shall be erected around all sides of the roof work area.
1926.502(f)(1)(i)When mechanical equipment is not being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge.
1926.502(f)(1)(ii)When mechanical equipment is being used, the warning line shall be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.
1926.502(f)(1)(iii)Points of access, materials handling areas, storage areas, and hoisting areas shall be connected to the work area by an access path formed by two warning lines.
1926.502(f)(1)(iv)When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, shall be placed across the path at the point where the path intersects the warning line erected around the work area, or the path shall be offset such that a person cannot walk directly into the work area.
1926.502(f)(2)Warning lines shall consist of ropes, wires, or chains, and supporting stanchions erected as follows:
1926.502(f)(2)(i)The rope, wire, or chain shall be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;
1926.502(f)(2)(ii)The rope, wire, or chain shall be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;
1926.502(f)(2)(iii)After being erected, with the rope, wire, or chain attached, stanchions shall be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;
1926.502(f)(2)(iv)The rope, wire, or chain shall have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, shall be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and
1926.502(f)(2)(v)The line shall be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

## Slide 13: Controlled Access Zones 1
A controlled access zone is a work area in which certain types of work may take place without using conventional fall protection systems. 1926.502(g)
    Overhand bricklaying and related work;
    Leading edge work;
    Residential construction; and
    Precast concrete erection.
Worker access to these areas must be carefully controlled.
    For example, a controlled access zone would be designated where overhand bricklaying was occurring without the protection of guardrails. In this example, only masons and other workers actually engaged in the bricklaying would be allowed in the controlled access zone.
    When used to control access to areas where leading edge and other operations are taking place, the controlled access zones must be defined by a control line or by any other means that restricts access.
Fall Protection Systems II

## Slide 14: Controlled Access Zones 2
When control lines are used to define a controlled access zone, they must be erected at least 6 feet and no more than 25 feet from the unprotected or leading edge, except:
    When precast concrete members are being erected, the control line is to be erected at least 6 feet and no more than 60 feet or half the length of the member being erected, whichever is less, from the leading edge.
The control line must extend along the entire length of and approximately parallel to the unprotected side or leading edge and be connected on each side to a guardrail system or wall.
1926.502(g)(1)
Fall Protection Systems II

## Slide 15: Controlled Access Zones 3
When controlled access zones are used to limit access to areas where overhand bricklaying and related work are taking place:
    A control line must be erected to define the work zone and must be erected at least 10 feet and no more than 15 feet from the working edge.
    The control lines must be erected approximately parallel to the working edge and must extend for a distance sufficient to enclose all workers performing overhand bricklaying and related work at the working edge.
    Additional control lines must be erected at each end of the controlled access zone to enclose the work area.
    Only workers engaged in overhand bricklaying or related work are permitted in the controlled access zone.
    1926.502(g)(2)
Fall Protection Systems II

## Slide 16: Controlled Access Zones 4
Control lines must consist of ropes, wires, tapes, or equivalent materials, and supporting stanchions. When used, each control line must:
    Be flagged or otherwise clearly marked at not more than 6-foot intervals with high-visibility material.
    Be rigged and supported in such a way that the lowest point (including sag) is not less than 39 inches from the walking or working surface; and the highest point is not more than 45 inches, or more than 50 inches when overhand bricklaying operations are being performed, from the walking or working surface.
    Have a breaking strength of at least 200 pounds.
Fall Protection Systems II

## Slide 17: Safety Monitoring Systems 1
A safety monitoring system uses a competent person as a safety monitor who can recognize and warn workers of fall hazards.
Safety monitoring systems are typically used as part of fall protection plans during precast concrete erection work, leading edge work, and residential construction work when conventional fall protection is infeasible or would create a greater hazard and alternative measures (such as scaffolds, ladders, or vehicle mounted work platforms) are not used.
Fall Protection Systems II

## Slide 18: Safety Monitoring Systems 2
When conducting roofing work on a flat or low sloped roof that is 50 feet or less in width, a safety monitoring system may be used as a stand alone fall protection technique.
Only workers engaged in low-sloped roofing work and workers performing the specific job tasks covered by a fall protection plan are allowed in an area where workers are being protected by a safety monitoring system.
Safety Monitor cannot be performing other tasks while being the safety monitor.
Fall Protection Systems II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 19: Safety Monitoring Systems 3
The worker designated as the safety monitor:
    May not perform other job tasks that could take attention away from the monitoring function.
    Must be on the same surface and within sight of the employees.
    Close enough to communicate orally with the employees.
Safety Monitor cannot be performing other tasks while being the safety monitor.
Fall Protection Systems II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 20: Safety Monitoring Systems 4
May be used on flat and low slope roofs.
Safety monitoring should be used sparingly.
Employees must comply promptly with warnings and directions.
Roof sections to be designated for protection under safety monitoring must be less than 50 feet in width.
Large roofs can be broken into sections.
Fall Protection Systems II
Notes: 1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.
1926.502(h)(2)Mechanical equipment shall not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.
1926.502(h)(3)No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, shall be allowed in an area where an employee is being protected by a safety monitoring system.
1926.502(h)(4)Each employee working in a controlled access zone shall be directed to comply promptly with fall hazard warnings from safety monitors.

## Slide 21: Covers 1
A hole is a gap or void 2 inches or more in its least dimension in a floor, roof, deck, or other walking/working surface that is hazardous because:
    Workers can fall through the hole;
    The hole’s design can create a trip hazard; and
    Objects can fall through the hole and injure workers below.
Workers are protected from the hazards associated with holes by the use of covers, personal fall protection or guardrail systems.
Fall Protection Systems II
Notes: 1926.502(i)"Covers." Covers for holes in floors, roofs, and other walking/working surfaces shall meet the following requirements:
1926.502(i)(1)Covers located in roadways and vehicular aisles shall be capable of supporting, without failure, at least twice the maximum axle load of the largest vehicle expected to cross over the cover.
1926.502(i)(2)All other covers shall be capable of supporting, without failure, at least twice the weight of employees, equipment, and materials that may be imposed on the cover at any one time.
1926.502(i)(3)All covers shall be secured when installed so as to prevent accidental displacement by the wind, equipment, or employees.
1926.502(i)(4)All covers shall be color coded or they shall be marked with the word "HOLE" or "COVER" to provide warning of the hazard. Note: This provision does not apply to cast iron manhole covers or steel grates used on streets or roadways.

## Slide 22: Covers 2
Fall Protection Systems II
Notes: 1926.502(i)"Covers." Covers for holes in floors, roofs, and other walking/working surfaces shall meet the following requirements:
1926.502(i)(1)Covers located in roadways and vehicular aisles shall be capable of supporting, without failure, at least twice the maximum axle load of the largest vehicle expected to cross over the cover.
1926.502(i)(2)All other covers shall be capable of supporting, without failure, at least twice the weight of employees, equipment, and materials that may be imposed on the cover at any one time.
1926.502(i)(3)All covers shall be secured when installed so as to prevent accidental displacement by the wind, equipment, or employees.
1926.502(i)(4)All covers shall be color coded or they shall be marked with the word "HOLE" or "COVER" to provide warning of the hazard. Note: This provision does not apply to cast iron manhole covers or steel grates used on streets or roadways.

## Slide 23: Covers 3
The following types of holes are commonly found at construction worksites:
    Holes cut (or constructed) in floors to receive equipment or ducts and for future access points (e.g., openings for stairs that will be installed later);
    Holes cut in roofs in preparation for installing skylights, ventilation units, and other features or equipment;
    Excavations for pits, wells, or shafts (e.g., caissons);
    Excavations or cuts in roadways.
Fall Protection Systems II

## Slide 24: Covers 4
Effective hole covers are: 1926.502(i)
    Large enough to provide appropriate overlap to prevent workers from falling through.
    Strong enough to support at least twice the anticipated weight imposed by the heaviest load .
    Left in place over the hole until access is needed.
    Inspected periodically to identify deterioration.
    Secured (side to side and up/down) and do not create trip hazards.
    Clearly marked as hole covers. (Consider Non-English marking)
Fall Protection Systems II

## Slide 25: Protection from Falling Objects 1
Toeboards, when used as falling object protection, shall be erected along the edge of the overhead walking/working surface protect employees below.
    At least 50 pounds applied in any downward or outward direction at any point along the toeboard.
    Minimum of 3 1/2 inches in vertical height from their top edge to the level of the walking/working surface.
    They shall have not more than 1/4 inch clearance above the walking/working surface.
    They shall be solid or have openings not over 1 inch (2.5 cm) in greatest dimension.
Fall Protection Systems II

## Slide 26: Protection from Falling Objects 2
1926.502(j)(1)
Where tools, equipment, or materials are piled higher than the top edge of a toeboard, paneling or screening shall be erected from the walking/working surface or toeboard to the top of a guardrail system's top rail or midrail, for a distance sufficient to protect employees below.
Fall Protection Systems II

## Slide 27: Protection from Falling Objects 3
Guardrail systems, when used as falling object protection, shall have all openings small enough to prevent passage of potential falling objects. 1926.502(j)(5)
During the performance of overhand bricklaying and related work:
    No materials or equipment except masonry and mortar shall be stored within 4 feet (1.2 m) of the working edge.
    Excess mortar, broken or scattered masonry units, and all other materials and debris shall be kept clear from the work area by removal at regular intervals.1926.502(j)(6)
Fall Protection Systems II

## Slide 28: Protection from Falling Objects 4
During the performance of roofing work:
    Materials and equipment shall not be stored within 6 feet (1.8 m) of a roof edge unless guardrails are erected at the edge.
    Materials which are piled, grouped, or stacked near a roof edge shall be stable and self-supporting.
Canopies, when used as falling object protection, shall be strong enough to prevent collapse and to prevent penetration by any objects which may fall onto the canopy.
Fall Protection Systems II

## Slide 29: Fall Protection Plan 1
Allowed for:
    Leading Edge Work
    Pre-Cast Concrete Erection
    Residential Construction
Site specific written fall plans are considered an alternative for these activities.
Fall Protection Systems II

## Slide 30: Fall Protection Plan 2
If the employer can demonstrate that it is infeasible or creates a greater hazard to use the required fall protection systems, the employer must instead develop and implement a written site-specific fall protection plan in accordance with 29 CFR 1926.502(k).
    OSHA does not consider "economic infeasibility" to be a basis for failing to provide conventional fall protection.
    Note: There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the fall protection systems.
Fall Protection Systems II

## Slide 31: Fall Protection Plan 3
Fall Protection Systems II

## Slide 32: Fall Protection Plan 4
Written by a qualified person
Shall identify each location where conventional fall protection systems cannot be used and designate them Controlled Access Zones (CAZ).
Implement a safety monitoring system where no other alternative measure has been implemented.
Shall identify all workers designated to work in the CAZ.
Shall be reviewed and updated as appropriate if a fall, or near miss, occurs.
Fall Protection Systems II

## Slide 33: Fall Protection Plan 5
Sample fall plans are provided in OSHA Standard Subpart M – Appendix E, for:
    Residential Construction and;
    Pre-Cast Concrete Erection.
Fall Protection Systems II

## Slide 34: Fall Protection Training Requirements 1
The employer shall provide a training program for each employee who might be exposed to fall hazards.
    Enable each employee to recognize the hazards of falling; and
    Utilize the proper procedures to be followed in order to minimize these hazards.
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 35: Fall Protection Training Requirements 2
The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
    The nature of fall hazards in the work area;
    The correct procedures for the fall protection systems to be used;
    The role of each employee in the safety monitoring system when this system is used;
    The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 36: Fall Protection Training Requirements 3
The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
    The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
    The role of employees in fall protection plans;
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 37: Fall Protection Training Requirements 4
Certification of training
    The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record.
    The written certification record shall contain:
      Name or other identity of the employee trained,
      The date(s) of the training, and
      The signature of the person who conducted the training or the signature of the employer.
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 38: Fall Protection Training Requirements 5
Certification of training
    If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
    The latest training certification shall be maintained.
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 39: Fall Protection Training Requirements 6
When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required, the employer shall retrain each such employee.
Circumstances where retraining is required include, but are not limited to, situations where:
    Changes in the workplace render previous training obsolete; or
    Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
    Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Fall Protection Systems II
Notes: 1926.503(a)Training program.
1926.503(a)(1)The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
1926.503(a)(2)The employer shall assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:
1926.503(a)(2)(i)The nature of fall hazards in the work area;
1926.503(a)(2)(ii)The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;
1926.503(a)(2)(iii)The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;
1926.503(a)(2)(iv)The role of each employee in the safety monitoring system when this system is used;
1926.503(a)(2)(v)The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;
1926.503(a)(2)(vi)The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and
1926.503(a)(2)(vii)The role of employees in fall protection plans;
1926.503(a)(2)(viii)The standards contained in this subpart.
1926.503(b)Certification of training.
1926.503(b)(1)The employer shall verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record shall contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of the employer. If the employer relies on training conducted by another employer or completed prior to the effective date of this section, the certification record shall indicate the date the employer determined the prior training was adequate rather than the date of actual training.
1926.503(b)(2)The latest training certification shall be maintained.
1926.503(c)Retraining. When the employer has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, the employer shall retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:
1926.503(c)(1)Changes in the workplace render previous training obsolete; or
1926.503(c)(2)Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or
1926.503(c)(3)Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.
Note: The following appendices to subpart M of this part serve as non-mandatory guidelines to assist employers in complying with the appropriate requirements of subpart M of this part.
[59 FR 40738, Aug. 9, 1994; 60 FR 5131, Jan. 26, 1995]

## Slide 40: Questions?
Fall Protection Systems II