## Slide 1: Operations with Fall Hazards
Wood Frame Construction
Fall Prevention in Construction

## Slide 2: Learning Objectives
Understand how OSHA defines residential construction
Understand the proper use of guardrails during framing operations
Identify best practices during roof truss installation
Understand the proper use of personal fall arrest systems (PFAS) during roofing activities
Operations with Fall Hazards – Wood Frame Construction

## Slide 3: Greater Hazard
If the employer can demonstrate that it is infeasible or creates a greater hazard to use the required fall protection systems, the employer must instead develop and implement a written site-specific fall protection plan in accordance with 29 CFR 1926.502(k).
    OSHA does not consider "economic infeasibility" to be a basis for failing to provide conventional fall protection. There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the fall protection systems.
    OSHA expects that the fall protection methods listed in 1926.501(b)(13) can be used without significant safety or feasibility problems for the vast majority of residential construction activities.
Operations with Fall Hazards – Wood Frame Construction
Notes: 29 CFR 1926.501(b)(13), Residential construction fall protection states “ There is a presumption that it is feasible and it will not create a greater hazard to implement fall protection systems, Accordingly, the employer has the burden of establishing that it is appropriate to implement a fall protection plan which meets the requirements of paragraph 1926.502(k)”
The Agency has never been convinced that there are significant safety or feasibility problems with the use of conventional fall protection equipment for the vast majority of residential construction activities.
But, we also acknowledge that there may be isolated situations where it may be infeasible or create a greater hazard to use conventional fall protection in residential construction. We believe that 29 CFR 1926.501(b)(13) provides sufficient flexibility to accommodate employers in those rare situations where they find it necessary to develop a site specific alternative fall protection plan .

## Slide 4: Definition of Residential Construction
In order to be classified as residential construction, two elements must be met:
    The end-use of the structure being built must be as a home, i.e., a dwelling; and
    The structure being built must be constructed using traditional wood frame construction materials and methods.
      The limited use of steel I-beams to help support wood framing does not disqualify a structure from being considered residential construction.
Operations with Fall Hazards – Wood Frame Construction
Notes: The end- use of the structure being built must be as a home, i.e., a dwelling … and,
The structure must be constructed using traditional wood frame construction materials and methods.
The limited use of steel I-beams to help support wood framing does not disqualify a structure from being considered residential construction.

## Slide 5: Deck Protection
All open edges and holes must be protected
Guardrails or other forms of fall protection must be provided
Protect the Edge
Protect the Hole
Operations with Fall Hazards – Wood Frame Construction
Notes: All edges and holes must be protected immediately after they’re created.

## Slide 6: Guardrail Systems
Here we see a floor perimeter completely protected by a guardrail system.
Operations with Fall Hazards – Wood Frame Construction
Notes: Here we see a 2nd AND 3RD floor perimeters completely protected by a guard rail system.

## Slide 7: Guardrails for Edges
These guardrails were set in a way that the walls could be set without removing them.
Operations with Fall Hazards – Wood Frame Construction

## Slide 8: Fall Hazard
Stud walls with 24” OC studs for non-load bearing walls must have guardrails.
Any opening over 19” wide must be guarded
Stud walls on 16” centers are acceptable.
1926.502(b)(2)(iii)
Operations with Fall Hazards – Wood Frame Construction
Notes: Falling from roofs is not the only area where fatalities have occurred. Open sides like this must be protected.

## Slide 9: Other Work Methods 1
Here is a guardrail system still in place that allows installation of dry wall and painting before installing the permanent handrail and removing the guardrail.
Operations with Fall Hazards – Wood Frame Construction
Notes: Here is the same system still in place through Mechanical, Electrical, Plumbing installation and dry wall.
Priming and painting can be done before installing the permanent handrail and removal of the guardrail.

## Slide 10: Fall Hazards
Not Good!!
Stairways must have railings before they can be used.
Floor holes must be protected immediately as decking is constructed around the hole.
Operations with Fall Hazards – Wood Frame Construction

## Slide 11: Guardrail Systems 1
Operations with Fall Hazards – Wood Frame Construction

## Slide 12: Guardrail Systems 2
Brackets and boots are available for guardrail systems that can either be side mounted or deck mounted.
Employers should look to the manufacturer’s instructions for proper installation.
Operations with Fall Hazards – Wood Frame Construction
Notes: The ability to be either side mounted or deck mounted allows flexibility to employers when using the engineered guardrail systems we just observed.
Either way, consult the manufacturer’s instructions or a registered professional engineer to ensure proper installation.

## Slide 13: Window Guard Rails
Window openings less than 39” high must be guarded
Operations with Fall Hazards – Wood Frame Construction

## Slide 14: Stay Off Top Plates
These workers are standing on the top plates of the walls to install trusses.
Workers should instead work from scaffolds or ladders.
Operations with Fall Hazards – Wood Frame Construction
Notes: There is no need to work from top plates. Ladders or scaffolds can be used.
There are several residential fall protection videos available from the State of Washington. Consider enhancing framing safety by showing an example for residential framing safety which is 13 minutes long and can be found at the following link. https://fortress.wa.gov/lni/shrl/VideoDetails.aspx?VideoID=850

## Slide 15: Installing Roof Trusses
Workers installing roof trusses from interior bracket scaffolds or ladders.
Operations with Fall Hazards – Wood Frame Construction

## Slide 16: Wall or Bracket Scaffolds
Here are examples of a wall bracket or top plate, scaffold systems.
Operations with Fall Hazards – Wood Frame Construction
Notes: Here are examples of wall bracket, or top plate scaffold systems.

## Slide 17: Other Work Methods 2
These workers are working from bracket/top plate scaffold systems.
Guardrails must be able to support 200 pounds in all directions.
Operations with Fall Hazards – Wood Frame Construction
Notes: Some contractors are using these systems for rolling trusses and cutting rafter tails.
1926.502(b)(3)
Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)
When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)
Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.

## Slide 18: Climbing on Trusses
Workers installing trusses should not stand on truss cords, especially while the truss is still supported on a crane.
Employees should work from ladders or scaffolds or work platforms installed in the trusses.
Operations with Fall Hazards – Wood Frame Construction
Notes: Workers can easily slip off truss cords.

## Slide 19: Truss Collapse
Collapses can occur from failure to adequately brace or from an overload.
Collapse of the truss system can result in serious injuries or death.
Operations with Fall Hazards – Wood Frame Construction
Notes: Truss systems can collapse

## Slide 20: Use of Guardrails
Engineered guardrail systems allow easy access for sheathing, roofing and utility installation.
Multiple trades can be protected by these kinds of systems.
Operations with Fall Hazards – Wood Frame Construction
Notes: The positioning of this guard rail system allows easy access for sheathing, roofing and utility installation.

## Slide 21: Fall Arrest System Anchors - Wood Frame
Wood members must be evaluated to assure that can support the forces imposed by fall arrest anchors.
Operations with Fall Hazards – Wood Frame Construction
Notes: Here are examples of various anchorage devices. All anchorage points must be capable of supporting at least 5,000 pounds per employee attached or 2x the intended load with (twice the potential impact energy of an employee free falling a distance of six feet, or the free fall distance permitted by the system whichever is less).
All anchor points should be installed under the supervision of “qualified person” and always follow the manufacturer’s instructions for installation, testing and safe use guidelines.

## Slide 22: Anchors
An example of a spreader attached to roof trusses.
Manufacturer’s requirements must be met.
NOTE:
    Truss systems and individual members must be evaluated to assure that they can support the forces imposed by fall arrest anchors
Operations with Fall Hazards – Wood Frame Construction
Notes: There are serious concerns about stability of the truss system if it is not adequately braced. The attachment points may overload the truss chord member’s ability to support it in a fall

## Slide 23: Personal Fall Arrest System Anchor Point
This is a 900 lb. Anchor
Anchors must be capable of supporting at least 5,000 pounds per employee attached for fall arrest, or must be designed and used:
    As part of a complete personal fall arrest system which maintains a safety factor of at least two.
    Or under the supervision of a qualified person.
Employers should look to the manufacturer’s instructions or the recommendations of a properly qualified person for proper installation.
Operations with Fall Hazards – Wood Frame Construction
Notes: 1926.502(d)(15): Proper installation of the Anchorage point is critical to the success of this system. It must be designed and installed to support the twice the impact load – twice the potential impact energy of an employee free falling a distance of six feet, or the free fall distance permitted by the system whichever is less - that would be applied to it if a worker fell. Consulting the manufacturer’s instructions or a registered professional engineer or properly qualified person with an engineering background and the ability to determine load forces and support criteria will ensure this critical component is properly installed and maintained.

## Slide 24: Roof Anchors
Operations with Fall Hazards – Wood Frame Construction

## Slide 25: Roof Fall Restraint
Workers are restrained from reaching the edge.
If they can reach the edge, full fall arrest must be implemented
Operations with Fall Hazards – Wood Frame Construction
Notes: The photo in the lower left may not depict the safe use of a fall restraint in that there appears to be too much slack in the system near the rake edge. The system tethers a worker in a manner that will not allow a fall of any distance. When rope grabs are used they must be set in a manner that allows minimal slack in a line to keep a user away from an edge of a structure. The Anchorage design can be less than that of an anchorage for a PFAS, thus a failure could result in a fall with arrest forces applied.
In a November 2, 1995, interpretation letter to Mr. Dennis Gilmore, OSHA suggested that, at a minimum, a fall restraint system have the capacity to withstand at least 3,000 pounds or twice the maximum expected force that is needed to restrain the person from exposure to the fall hazard. In determining this force, consideration should be given to site-specific factors such as the force generated by a person (including his or her tools, equipment and materials) walking, slipping, tripping, leaning, or sliding along the work surface.

## Slide 26: Use of Retractables
Anchorage must be able to support at least 3,000 lbs.
Retractables CANNOT be used in a restraint set.
Operations with Fall Hazards – Wood Frame Construction
Notes: … when there are systems available to protect them from falling and hitting the ground.

## Slide 27: Shingle Demolition or Tear-off
Fall protection is required during all roof operations
Incomplete Fall Protection
Operations with Fall Hazards – Wood Frame Construction
Notes: Picture in bottom left photo is a 4:12 pitch would could qualify for a safety monitoring system.

## Slide 28: Wood Frame Fall Anchors
These anchor straps are installed during framing and available for use during roofing and siding.
NOTE:
    Wood members must be evaluated to assure that they can support the forces imposed by fall arrest anchors
Operations with Fall Hazards – Wood Frame Construction

## Slide 29: Ladder Jack Scaffolds
Platforms shall not exceed a height of 20 feet.
Workers on ladder jacks must use a PFAS.
Fall arrest must be tied-off above.
Ladders used to support ladder jacks shall be placed, fastened and equipped with devices to prevent slipping.
Operations with Fall Hazards – Wood Frame Construction
Notes: 1926.451(g)(1)(i) Each employee on a boatswains' chair, catenary scaffold, float scaffold, needle beam scaffold, or ladder jack scaffold shall be protected by a personal fall arrest system;
1926.452(k) "Ladder jack scaffolds."
1926.452(k)(1) Platforms shall not exceed a height of 20 feet (6.1 m).
1926.452(k)(2) All ladders used to support ladder jack scaffolds shall meet the requirements of subpart X of this part -- Stairways and Ladders, except that job-made ladders shall not be used to support ladder jack scaffolds.
1926.452(k)(3) The ladder jack shall be so designed and constructed that it will bear on the side rails and ladder rungs or on the ladder rungs alone. If bearing on rungs only, the bearing area shall include a length of at least 10 inches (25.4 cm) on each rung.
1926.452(k)(4) Ladders used to support ladder jacks shall be placed, fastened, or equipped with devices to prevent slipping.
1926.452(k)(5) Scaffold platforms shall not be bridged one to another.

## Slide 30: Pump-jack Scaffolds
Pump jacks are safer than ladder jacks.
There are fall issues when anchoring pump jack poles.
Operations with Fall Hazards – Wood Frame Construction
Notes: Pump jacks are a popular system used by many contractors to install building wrap and siding. Some contractors have used different variations of the pump jack that allow them to jack it up to just under the fascia and be used as catch platforms. There the system can be used as perimeter protection while sheathing and roofing operations are performed.
Remember the potential “electrocution hazards resulting from contact with power lines” while standing or moving poles and access ladders.

## Slide 31: Questions?
Operations with Fall Hazards – Wood Frame Construction