## Slide 1: Duty to Have Fall Protection
Fall Prevention in Construction

## Slide 2: What is Fall Protection?
A series of reasonable steps taken to cause elimination or control of the injurious effects of an unintentional fall while accessing or working at height.
Duty to Have Fall Protection
Notes: A great OSHA video giving a wonderful overview of the standard

## Slide 3: What is Fall Protection? 2
Duty to Have Fall Protection

## Slide 4: Fall Protection Program
Does OSHA require your company to have a written Fall Protection/Prevention Program?
    No but it does require:
      The employer shall provide a training program for each employee who might be exposed to fall hazards. The program shall enable each employee to recognize the hazards of falling and shall train each employee in the procedures to be followed in order to minimize these hazards.
      Standard: 1926.503(a)(1)
Duty to Have Fall Protection

## Slide 5: Fall Protection Program 2
Best practice is to have a written program that describes at minimum:
    Hierarchy of Fall Protection Controls;
    Employee Training and Responsibilities;
    Employer Responsibilities; and
    Fall Protection / Prevention Systems Used
      Guardrails, PFAS, Rescue, Positioning, Warning lines, Etc…
Duty to Have Fall Protection

## Slide 6: Hierarchy of Fall Protection Controls
Priority | Control | Examples
First | Eliminate the fall hazard | Bring work to ground level; Use tools to eliminate work above ground level
Second | Passive fall restraint | Install physical barriers, such as guardrails or parapets, to prevent falls
Third | Active fall restraint | Use a restraint system (e.g., full-body harness, lanyard and anchor) to prevent falls
Fourth | Fall arrest | Use a personal fall arrests system or safety net to minimize fall injuries
Fifth | Controlled access zones (CAZ) a last resort | When fall protection is not feasible, provide adequate training, on-site supervision, signage and visible barriers to preclude workers from fall hazard zones
Duty to Have Fall Protection

## Slide 7: Hierarchy of Fall Protection Controls 2
Duty to Have Fall Protection
Notes: Change graphic to add titles Active and Passive

## Slide 8: Specific Areas
Walking Working Surfaces
Leading Edges
Hoist Areas
Holes
Duty to Have Fall Protection

## Slide 9: Specific Areas 2
Formwork and Reinforcing Steel
Excavations
Dangerous Equipment
Duty to Have Fall Protection

## Slide 10: Specific Areas 3
Overhand bricklaying and related work
Roofing work on Low-slope roofs
Steep roofs
Precast concrete erection
Duty to Have Fall Protection

## Slide 11: Specific Areas 4
Residential construction
Wall openings
Protection from falling objects
Duty to Have Fall Protection

## Slide 12: Duty to Have Fall Protection 2
Walking Working Surfaces
    MUST have the strength and structural integrity to support employees safely.
Unprotected sides and edges.
    Protect employees from all open sides, floors, or edges which are 6 feet (1.8 m) or more above a lower level.
    Guardrail systems, Safety Net systems, or Personal Fall Arrest Systems (PFAS).
Duty to Have Fall Protection

## Slide 13: Duty to Have Fall Protection 3
Leading Edges – 29 CFR 1926.501(b)(2)
    Each worker constructing a leading edge 6 feet or more above a lower level must be protected by guardrail systems, safety net systems, or personal fall arrest systems.
    Exception: When the employer can demonstrate that it is infeasible or creates a greater hazard to use these systems, the employer must develop and implement a fall protection plan
Duty to Have Fall Protection

## Slide 14: Duty to Have Fall Protection 4
Hoist Areas – 29 CFR 1926.501(b)(3)
    Each worker in a hoist area must be protected from falling 6 feet or more by guardrail systems or personal fall arrest systems.
    What is guardrails are removed to land a load?
Duty to Have Fall Protection
Notes:     There may be times when the guardrail systems (or chain, gate, or guardrail) must be removed in whole or part to facilitate hoisting operations. For example, during the landing of materials, a worker may need to lean through the access opening or out over the edge of the access opening to receive or guide equipment and materials.

## Slide 15: Duty to Have Fall Protection 5
Holes – 29 CFR 1926.501(b)(4)
    Each worker on walking or working surfaces must be protected from falling through holes (including skylights) that are more than 6 feet above lower levels, by personal fall arrest systems, covers, or guardrail systems erected around such holes.
What is a “Hole”….
    Any Opening greater than 2 inches in any direction.
Duty to Have Fall Protection
Notes: Each worker on a walking or working surface must be protected from tripping in or stepping into or through holes (including skylights) by covers.

## Slide 16: Duty to Have Fall Protection 6
Excavations – 29 CFR 1926.501(b)(7)
    Each worker at the edge of an excavation 6 feet or more deep must be protected from falling by guardrail systems, fences, or barricades when the excavation cannot be readily seen because of plant growth or other visual barrier.
    Each worker at the edge of a well, pit, shaft, and similar excavation 6 feet or more deep must be protected from falling by guardrail systems, fences, or barricades, or covers. 29 CFR 1926.502(b)(7)(ii).
Duty to Have Fall Protection

## Slide 17: Duty to Have Fall Protection 7
Dangerous Equipment – 29 CFR 1926.501(b)(8)
    When working 6 feet or more above dangerous equipment, each worker must be protected by guardrail systems, safety net systems, or personal fall arrest systems.
Duty to Have Fall Protection
Notes: When working less than 6 feet above dangerous equipment, each worker must be protected from falling into or onto the dangerous equipment by a guardrail system or equipment guards.

## Slide 18: Duty to Have Fall Protection 8
Overhand Bricklaying and Related Work – 29 CFR 1926.501(b)(9)
    When workers perform overhand bricklaying and related work 6 feet or more above a lower level:
      They must be protected by guardrail systems, safety net systems, or personal fall arrest systems, or
      They must work in a controlled access zone (CAZ) All workers reaching more than 10 inches below the level of the walking or working surface on which they are working must be protected by a guardrail system, safety net system, or personal fall arrest system.
Duty to Have Fall Protection

## Slide 19: Duty to Have Fall Protection 9
Roofing Work on Low-Slope Roofs – 29 CFR 1926.501(b)(10)
    A low-slope roof has a slope less than or equal to 4 in 12 (vertical to horizontal). When engaged in roofing work on a low-slope roof that has one or more unprotected side or edge 6 feet or more above lower levels, workers must be protected from falling by:
      Guardrail systems, Safety net systems, Personal fall arrest systems,
OR
      A combination of conventional fall protection systems and warning line systems, or
      A warning line system and a safety monitoring system.
Duty to Have Fall Protection
Notes: When engaged in roofing work on low-slope roofs 50 feet or less in width, the use of a safety monitoring system without a warning line system is permitted.

## Slide 20: Duty to Have Fall Protection 10
Working on Steep Roofs – 29 CFR 1926.501(b)(11)
    A steep roof has a slope greater than 4 in 12 (vertical to horizontal). When working on a steep roof that has one or more unprotected side or edge 6 feet or more above lower levels, each worker must be protected by:
      Guardrail systems with toeboards,
      Safety net systems, or
      Personal fall arrest systems.
Duty to Have Fall Protection

## Slide 21: Duty to Have Fall Protection 11
Residential Construction – 29 CFR 1926.501(b)(13)
    Workers engaged in residential construction 6 feet or more above lower levels must be protected by conventional fall protection (i.e., guardrail systems, safety net systems, or personal fall arrest systems) unless another provision in 29 CFR 1926.501(b) provides for an alternative fall protection measure.
Duty to Have Fall Protection
Notes: Exception: When the employer can demonstrate that it is infeasible or creates a greater hazard to use these systems, the employer must develop and implement a site-specific fall protection plan which meets the requirements of 29 CFR 1926.502(k). See the section on Fall Protection Plans, below.

## Slide 22: Duty to Have Fall Protection 12
Residential Construction – 29 CFR 1926.501(b)(13)
    For purposes of determining the applicability of section 1926.501(b)(13), the term “residential construction” is interpreted as covering construction work that satisfies the following two elements:
      The end-use of the structure being built must be as a home, i.e., a dwelling; and
      The structure being built must be constructed using traditional wood frame construction materials and methods.
Duty to Have Fall Protection
Notes: The limited use of structural steel in a predominantly wood-framed home, such as a steel I-beam to help support wood framing, does not disqualify a structure from being considered residential construction.
For more information see OSHA’s Compliance Guidance for Residential Construction, STD 03-11-002.

## Slide 23: Duty to Have Fall Protection 13
Wall Openings – 29 CFR 1926.501(b)(14)
    Each worker working on, at, above, or near wall openings (including those with chutes attached), where the outside bottom edge of the wall opening is 6 feet or more above lower levels and the inside bottom edge of the wall opening is less than 39 inches above the walking or working surface, must be protected with a guardrail system, a safety net system, or a personal fall arrest system.
Duty to Have Fall Protection

## Slide 24: Duty to Have Fall Protection 14
Elevator Hoistways (fall protection) – 29 CFR 1926.501(b)(1)
    Each employee on a walking/working surface with an unprotected side or edge which is 6 feet (1.8 m) or more above a lower level shall be protected from falling by the use of guardrail systems, safely net systems, or personal fall arrest systems.
Duty to Have Fall Protection
Notes:     There may be times when the guardrail systems (or chain, gate, or guardrail) must be removed in whole or part to facilitate hoisting operations. For example, during the landing of materials, a worker may need to lean through the access opening or out over the edge of the access opening to receive or guide equipment and materials.

## Slide 25: Duty to Have Fall Protection 15
Elevator Hoistways (falling objects) – 29 CFR 1926.501(c) – (c)3
    When an employee is exposed to falling objects, the employer shall have each employee wear a hard hat and shall implement one of the following measures:
      Erect toe-boards, screens, or guardrail systems to prevent objects from falling from higher levels
      Barricade the area to which objects could fall
Duty to Have Fall Protection
Notes:     There may be times when the guardrail systems (or chain, gate, or guardrail) must be removed in whole or part to facilitate hoisting operations. For example, during the landing of materials, a worker may need to lean through the access opening or out over the edge of the access opening to receive or guide equipment and materials.

## Slide 26: Protection from Falling Objects
Guardrails – 29 CFR 1926.502(j)(5)
    When guardrail systems are used to prevent materials from falling from one level to another, any openings must be small enough to prevent passage of falling objects.
Duty to Have Fall Protection

## Slide 27: Protection from Falling Objects 2
Roofing Work – 29 CFR 1926.502(j)(7)
    During roofing work, materials and equipment must not be stored within 6 feet of a roof edge unless guardrail systems are erected at the edge. Any materials piled, grouped, or stacked near a roof edge must be stable and self-supporting.
Canopies – 29 CFR 1926.502(j)(8)
    When used as protection from falling objects, canopies must be strong enough to prevent collapse and to prevent penetration by any objects that may fall onto them.
Duty to Have Fall Protection

## Slide 28: Protection from Falling Objects 3
Toeboards – 29 CFR 1926.502(j)(1) through (4)
    When toeboards are used as protection from falling objects, they must be erected along the edges of the overhead walking or working surface for a distance sufficient to protect workers working below. Other criteria include:
      50 pounds.
      At least 3.5 inches
      Where tools, equipment, or materials are piled higher than the top edge of a toeboard, paneling or screening must be erected from the walking or working surface or toeboard to the top of a guardrail system’s top rail or midrail, for a distance sufficient to protect workers below.
Duty to Have Fall Protection

## Slide 29: Questions?
Duty to Have Fall Protection