## Slide 1: Operations with Fall Hazards
Concrete and Steel Erection
Fall Prevention in Construction

## Slide 2: Learning Objectives
Understand the OSHA requirements for fall protection during concrete operations
    Working from Rebar
    Working on Forms
    Pre-Cast Concrete Erection
Understand the OSHA requirements for fall protection during steel erection
Identify best practices for protecting workers from falls performing concrete operations
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 3: Rebar Protection
Caps must protect from injury, especially impalement.
Mushroom caps are not allowed on low vertical bars.
Mushroom Cap
Reinforced Cap
Caps can pop
2x4 mount cap
OK
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Rebar caps must be able to with stand impalement if vertical.
The standard, 29 CFR 1926.701(b), states: "all protruding reinforcing steel, onto and into which employees could fall, shall be guarded to eliminate the hazard of impalement." The key words are "to eliminate the hazard of impalement." Exposure to impalement is always a consideration when employees are working above rebar or other sharp protrusions. The critical element when evaluating any job activity is the recognition or identification of impalement hazards and the exposure to employees. As you know, construction activities constantly change and contractors must remain aware of and provide protection from or alternative work practices to eliminate impalement hazards
When employees are working at any height above exposed rebar, fall protection/prevention is the first line of defense against impalement. Fall protection/prevention is also applicable when the rebar is below grade, e.g., footings or other excavations, where a fall into a trench would present an impalement hazard. When work is at grade, impalement exposure is dependent upon numerous situations and conditions; proximity of rebar to worker, height of rebar, e.g., working around rebar that is 3-6 feet high would not likely pose an impalement hazard. Rebar caps/covers are appropriate to prevent cuts, abrasions or other minor injuries when working at grade and there is no impalement hazard.

## Slide 4: Positioning Systems
Positioning Devices Provide Hands-free Work
Additional Fall Protection (tie-off) may be required to move point-to-point or access another area.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 5: Working on Rebar Wall Cages
Workers must be protected above 6 feet when working on ALL rebar assemblies
Workers may move point-to-point on built-in place rebar assemblies up to 24 ft. if they are ladder like.
But only 6 feet if the assembly is built on the ground and lifted into place.
    (OSHA Interps 6-20-95 & 5-19-97)
Operations with Fall Hazards – Concrete and Steel Erection
Notes: OSHA Interpretation:
Through the promulgation of the existing standard, section §1926.501(b)(5), OSHA clearly indicates that Subpart M applies to construction work performed on vertical surfaces, such as rebar structures. In response to your December 1994 presentation of information, the Agency issued a letter acknowledging that fall protection is not necessary for employees climbing or moving on built-in-place rebar assemblies at heights below 24 feet.
OSHA Interpretation:
The Occupational Safety and Health Administration's letter to Mr. Codding and a compliance interpretation issued on February 2, 1995, apply
to built-in-place rebar assemblies only. You are correct in your understanding that this policy does not apply to rebar assembly sections built
on the ground and which are then lifted into place by a crane or other equipment. In this situation fall protection is required at all times for
employees working above six feet in height (including while climbing or moving point to point)

## Slide 6: Fall Protection on Vertical Forms
Hooked
Workers must be protected when 6’ or higher.
They must position off before working on column and wall forms.
If the vertical form is near an edge, the employee must establish fall protection before he climbs the form.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 7: Construction of Shored Forming
Employees are exposed to major falls while constructing form work around perimeter columns.
They must have fall protection
This worker is tied off to column behind the edge.
Fall
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 8: Column Forms
Fall hazards?
Scaffolds or lifts help reduce fall exposures.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Shored Forming systems are temporary structures meeting the definition of a scaffold. Fall protection must be considered based on those requirements.

## Slide 9: Safe-T-Straps
Safety straps are effective, simple anchors in concrete construction.
They slip over rebar and are then embedded in the concrete.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 10: Potential Trip Hazards
There are potential trip hazards on reinforced floors.
Temporary walkways are a good hazard control.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Workers can slip and get feet between rebar that can cause a serious leg injury.

## Slide 11: Pre-Cast Concrete Erection - Controlled Access Zones
Employees may work in a CAZ under a qualified fall plan when it can be shown that standard fall protection is infeasible.
Plan must be site specific.
All employees must be trained in the safe erection of pre-cast concrete.
A safety monitor must oversee the fall safety.
Warning lines must be set along the edges and guardrails installed as soon as possible.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.501(b)(12)
"Precast concrete erection." Each employee engaged in the erection of precast concrete members (including, but not limited to the erection of wall panels, columns, beams, and floor and roof "tees") and related operations such as grouting of precast concrete members, who is 6 feet (1.8 m) or more above lower levels shall be protected from falling by guardrail systems, safety net systems, or personal fall arrest systems, unless another provision in paragraph (b) of this section provides for an alternative fall protection measure. Exception: When the employer can demonstrate that it is infeasible or creates a greater hazard to use these systems, the employer shall develop and implement a fall protection plan which meets the requirements of paragraph (k) of 1926.502.
Note: There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the above-listed fall protection systems. Accordingly, the employer has the burden of establishing that it is appropriate to implement a fall protection plan which complies with 1926.502(k) for a particular workplace situation, in lieu of implementing any of those systems.

## Slide 12: Setting & Receiving Planks
Approach the plank when it is waist high.
Restraint should always be used.
The Safety Monitor oversees the safety of the setting process if working under a plan.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 13: Steel Erection

## Slide 14: Shear Studs
Shear studs are commonly used in construction for composite concrete decks.
But they are a tripping hazard.
Workers may not walk on beams with studs or other protrusions.
There must be a work alternate platform.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Discuss that shear studs are very common in bridge construction. In many parts of the country it is common that these studs be installed at the fabricator.
OSHA has rescinded a previous interpretation that called the installation De minimus
This Instruction does not alter any other provisions of OSHA Instruction CPL 02-01-034 (formerly CPL 2-1.34),
which remains in full force and effect. The revision to Question and Answer #23 is effective as of April 30, 2010.
The de minimis policy described in the original version of Question and Answer #25 will continue to apply where
the component was fabricated with shear connectors or other similar devices prior to April 30, 2011, or where
the contract date for fabrication of the component with factory-installed shear connectors or other similar
devices was prior to April 30, 2011. In all other instances the revised version of Question and Answer #25 is
effective as of April 30, 2010. The text of the OSHA Instruction CPL 02-01-034 (formerly CPL 2-1.34) on the web
will be amended accordingly within two weeks of the issuance date. In addition, OSHA Instruction CPL 02-01-
046 (Sept. 30, 2009) is cancelled, effective as of April 30, 2010.
While OSHA encourages employers to exceed the fall protection requirements of the standard and have
all workers use fall protection, section 1926.754(c)(1) is an engineering control that helps prevent tripping,
which helps to prevent injury from falling on a shear connector and helps to prevent falls. Therefore, such an
employer would be required to comply with section 1926.754(c)(1).

## Slide 15: Joist As Fall Anchorages
Joists cannot be used as fall arrest anchorages unless there is written approval by a qualified person.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.757(a)(9) The joist may not be stable enough to support a 5,000 lb. Load. The top chord angles of the joist may also not hold a beam clamp or other device.

## Slide 16: Fall Protection on Metal Buildings
Purlins and girts may not be used as fall arrest anchorages unless approved by a qualified person.
May not walk on purlins until all permanent bridging has been installed and fall protection is provided.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 17: Fall Protection
Must be provided at 15 feet.
Exceptions (15 – 30 feet)
    Initial connecting
    Decking in a “Controlled Decking Zone”
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.760 Initial connecting is setting main support frame members such as columns, beams, joists, etc.

## Slide 18: Connectors
An employee who, working with hoisting equipment, is placing and connecting structural members and/or components.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Connectors are defined by work activity not by title. They are only a connector while actually doing connecting work under definition of the standard.
Connectors. Each connector shall:
1926.760(b)(1)
Be protected in accordance with paragraph (a)(1) of this section from fall hazards of more
than two stories or 30 feet (9.1 m) above a lower level, whichever is less;
1926.760(b)(2)
Have completed connector training in accordance with § 1926.761; and
1926.760(b)(3)
Be provided, at heights over 15 and up to 30 feet above a lower level, with a personal fall
arrest system, positioning device system or fall restraint system and wear the equipment
necessary to be able to be tied off; or be provided with other means of protection from
fall hazards in accordance with paragraph (a)(1) of this section.

## Slide 19: Connectors 2
Must be protected from fall hazards of more than two stories or 30 ft. above a lower level whichever is less;
Must have completed connector training;
Must be provided – at heights over 15 ft. and less than 30 ft. above a lower level – with a personal fall arrest system, positioning device system or fall restraint system; and
Must wear the equipment necessary to be tied off or provided with other means of fall protection.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.760(b) Read the text. Note that basically fall systems must be installed at 15 feet. So, there is no reason to allow the connector to work higher.
Connectors. Each connector shall:
1926.760(b)(1)
Be protected in accordance with paragraph (a)(1) of this section from fall hazards of more
than two stories or 30 feet (9.1 m) above a lower level, whichever is less;
1926.760(b)(2)
Have completed connector training in accordance with § 1926.761; and
1926.760(b)(3)
Be provided, at heights over 15 and up to 30 feet above a lower level, with a personal fall
arrest system, positioning device system or fall restraint system and wear the equipment
necessary to be able to be tied off; or be provided with other means of protection from
fall hazards in accordance with paragraph (a)(1) of this section.

## Slide 20: Using Lifts
Using lifts, where feasible, eliminates the need to climb on the steel and eliminates some fall protection issues.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 21: Fully Planked Decks
A fully planked or decked floor or safety nets shall be maintained within two stories or 30 feet, whichever is less, directly under any erection work being performed.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.754(b)(3)
within two stories or 30 feet, whichever is less. Section 1926.760 requires workers above 15 feet to be protected
from falls, with two exceptions: section 1926.760(b)(3) and (c) allows workers engaged in certain steel erection
activities (initial connecting; decking in a Controlled Decking Zone) below 30 feet to work without using fall
protection. Can an employer's requirement that all workers be protected by fall arrest systems, including those
engaged in connecting and decking, take the place of compliance with the 1926.754(b)(3) floor/net
requirement?
Answer: While OSHA encourages employers to exceed the fall protection requirements of the standard and have
all workers use fall protection, section 1926.754(b)(3) provides additional safeguards. Therefore, such an
employer would be required to comply with 1926.754(b)(3). However, compliance staff retain their normal
discretion to determine, on a case by case basis, that violations are de minimis where there is no direct or
immediate relationship to safety or health, and the employer's use of personal fall protection systems at all times
may be a factor in such a determination. See OSHA's Field Operations Manual, CPL 02-00-148 (Nov. 9, 2009),
section VIII.

## Slide 22: Controlled Decking Zone (CDZ)
A marked area in which initial installation and placement of metal deck may take place without fall protection.
Access to the zone is controlled.
No more than 90’ X 90’ wide.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 23: Controlled Decking Zone (CDZ) 2
The controlled decking zone (CDZ) is defined by a control line or by any other means that restricts access.
    A control line for a CDZ is erected not less than 6 feet (1.8 m) nor more than 90 feet from the leading edge.
    Control lines extend along the entire length of the unprotected or leading edge and are approximately parallel to the unprotected or leading edge.
    Control lines are connected on each side to a guardrail system, wall, stanchion or other suitable anchorage.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 24: Controlled Decking Zone (CDZ) 3
Control lines consist of ropes, wires, tapes, or equivalent materials, and supporting stanchions as follows:
    Each line is rigged and supported in such a way that its lowest point (including sag) is not less than 39 inches from the walking/working surface and its highest point is not more than 45 inches from the walking/working surface.
    Each line has a minimum breaking strength of 200 pounds.
    *Appendix D to Subpart R -- Illustration of the Use of Control Lines To Demarcate Controlled Decking Zones (CDZs): Non-mandatory Guidelines for Complying With § 1926.760(c)(3)
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 25: Decking
Can be done in a “Controlled Decking Zone” up to 30 feet. 1926.760(c)
Workers must be trained.
Workers must not cut holes or must cover all floor or deck holes immediately when formed.
Perimeter protections must be established as soon as possible.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 26: Controlled Decking Plan
Not required but advisable
Can be used between 15 & 30 feet.
Must be:
    Developed by a qualified person.
    Site Specific.
Must establish alternate procedures for fall protection.
Employees must complete CDZ training.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: Discuss the components of a Controlled Decking Plan.
Alternate procedures can include warning lines, safety monitoring, etc.

## Slide 27: Decking Gaps
Decking gaps must be filled.
Wire mesh, exterior plywood, or equivalent, shall be installed around columns where planks or metal decking do not fit tightly. 1926.501(b)(4) - "Holes."
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.754(e)(4)

## Slide 28: Decking Operations
Employees working over 30 feet must be protected by conventional fall protection. 1926.760(c)
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 29: Decking Pre-Engineered Buildings
Insulation and roof panels on Systems Engineered buildings fall under this section.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: This includes pre-engineered decks with insulation lay out.

## Slide 30: Simple Saver Plus Insulation Pre-Engineered Buildings
System creates a fall protection netting while holding insulation.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 31: Skyweb System Pre-Engineered Buildings
Acts as an internal safety net.
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 32: Use of Decking Systems (Pre-Engineered)
Mechanical decking systems and rolling scaffold systems eliminate many fall exposures on large pre-engineered roof decks.
Elaminator System
Operations with Fall Hazards – Concrete and Steel Erection

## Slide 33: Custody of Fall Protection
Controlling contractor must inspect and accept control and responsibility of the fall protection, such as cable guardrails, when steel erector leaves the site.
Controlling contractor must be sure that the cables meet standards before accepting.
Operations with Fall Hazards – Concrete and Steel Erection
Notes: 1926.760(g)
This is a potential liability issue.
Guardrail deflection is something that needs to be checked for compliance. Cables cannot deflect to below 39”

## Slide 34: Questions?
Operations with Fall Hazards – Concrete and Steel Erection