## Slide 1: Fall Protection Systems I
Fall Prevention in Construction
Criteria and Practices

## Slide 2: Learning Objectives
Understanding the basic and best practices associated with the following Fall Protection Systems:
    Guardrails
    PFAS
    Safety Nets
Fall Protection Systems I

## Slide 3: Do I really need Fall Protection?
I've carefully thought out all the angles.
Nothing could possibly go wrong, and it wouldn’t happen to me anyway
I've done it a thousand times.
I know what I’m doing, its what I've been trained to do my whole life.
Fall Protection Systems I

## Slide 4: Fall Protection Systems 1
Guardrail systems
Safety net systems
Personal fall arrest systems (PFAS)
Positioning device systems
Warning line systems
Fall Protection Systems I

## Slide 5: Fall Protection Systems 2
Controlled access zones
Safety monitoring systems
Covers
Protection from falling objects
Fall protection plan
Fall Protection Systems I

## Slide 6: Guardrail Systems 1
Posts – 8 feet apart.
Toprails – 42 inches + 3 inches, capable of withstanding 200 lbs of force.
Midrails – mid way between the top rail and the working surface and capable of withstanding 150 lbs of force.
Toeboards – 3 ½ inches high, nailed in place and installed flush with the working surface.
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 7: Guardrail Systems 2
When intermediate members (such as balusters) are used between posts, they must not be more than 19 inches apart.
    Other structural members (such as additional midrails and architectural panels) must be installed so that there are no openings in the guardrail system more than 19 inches wide.
When screens and mesh are used, they must extend from the top rail to the walking or working level and along the entire opening between top rail supports.
Guardrail systems must have a surface to protect workers from punctures or lacerations and to prevent clothing from snagging
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 8: Guardrail Systems 3
Top rails and midrails of guardrail systems must have a nominal diameter or thickness of at least 14 inch to prevent cuts and lacerations.
    Toprails – 42 inches + 3 inches,
    Midrails – mid way between the top rail and the working surface and capable of withstanding 150 lbs of force.
If wire rope is used for top rails, it must be flagged at not more than 6-foot intervals with high-visibility material.
If guardrail systems are used around holes being used as access points (such as ladderways), gates must be used. Alternatively, the point of access must be offset to prevent workers from accidentally walking straight into the hole.
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 9: Guardrail Systems 4
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 10: Guardrail Systems 5
1 ½” Outside Diameter Pipe
2” x 2” x ¼” Angles
Standard 2” x4”
Cable (minimum ¼”)
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 11: Guardrail Systems 6
Weighted Portable Guardrails
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 12: Guardrail Systems 7
When employees work above guardrails, they must be protected from falling over the guardrails.
Fall Protection Systems I
Notes: 1926.502(b)"Guardrail systems." Guardrail systems and their use shall comply with the following provisions:
1926.502(b)(1)Top edge height of top rails, or equivalent guardrail system members, shall be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph. Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, shall be increased an amount equal to the height of the stilts.
1926.502(b)(2)Midrails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members shall be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.
1926.502(b)(2)(i)Midrails, when used, shall be installed at a height midway between the top edge of the guardrail system and the walking/working level.
1926.502(b)(2)(ii)Screens and mesh, when used, shall extend from the top rail to the walking/working level and along the entire opening between top rail supports.
1926.502(b)(2)(iii)Intermediate members (such as balusters), when used between posts, shall be not more than 19 inches (48 cm) apart.
1926.502(b)(2)(iv)Other structural members (such as additional midrails and architectural panels) shall be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.
1926.502(b)(3)Guardrail systems shall be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.
1926.502(b)(4)When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail shall not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.
1926.502(b)(5)Midrails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members shall be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the midrail or other member.
1926.502(b)(6)Guardrail systems shall be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.
1926.502(b)(7)The ends of all top rails and midrails shall not overhang the terminal posts, except where such overhang does not constitute a projection hazard.
1926.502(b)(8)Steel banding and plastic banding shall not be used as top rails or midrails.
1926.502(b)(9)Top rails and midrails shall be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it shall be flagged at not more than 6-foot intervals with high-visibility material.
1926.502(b)(10)When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section shall be placed across the access opening between guardrail sections when hoisting operations are not taking place.
1926.502(b)(11)When guardrail systems are used at holes, they shall be erected on all unprotected sides or edges of the hole.
1926.502(b)(12)When guardrail systems are used around holes used for the passage of materials, the hole shall have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it shall be closed over with a cover, or a guardrail system shall be provided along all unprotected sides or edges.
1926.502(b)(13)When guardrail systems are used around holes which are used as points of access (such as ladderways), they shall be provided with a gate, or be so offset that a person cannot walk directly into the hole.
1926.502(b)(14)Guardrail systems used on ramps and runways shall be erected along each unprotected side or edge.
1926.502(b)(15)Manila, plastic or synthetic rope being used for top rails or midrails shall be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

## Slide 13: Safety Net Systems 1
Install as close as practicable under the walking/working surface and never more than 30 feet below.
Inspected once a week
Items that fall into the safety nets must be removed as soon as possible.
Fall Protection Systems I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 14: Safety Net Systems 2
Fall Protection Systems I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 15: Safety Net Systems 3
Outwards Extension of Safety Nets
Vertical distance to the net | Horizontal distance from the working edge
Upto 5 feet | 8 feet
Upto 10 feet | 10 feet
More than 10 feet | 13 feet
Fall Protection Systems I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 16: Safety Net Systems 4
Drop-testing is required to ensure that safety nets and safety net installations are working properly. See 29 CFR 1926.502(c)(4)(i) for more details.
    If an employer can demonstrate that it is unreasonable to perform a drop-test, then the employer or a designated competent person must certify that the net and its installation is in compliance with the standard.
    See 29 CFR 1926.502(c)(4)(ii) for more details on certification and certification records.
Fall Protection Systems I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 17: Safety Net Systems 5
To work properly, a safety net must have safe openings. Mesh openings must not exceed 36 square inches, and must not be longer than 6 inches on any side. Each opening, measured center-to-center of mesh ropes or webbing, must not exceed 6 inches. 29 CFR 1926.502(c)(7).
All mesh crossings must be secured to prevent the openings from enlarging. 29 CFR 1926.502(c)(7).
Use safety net (or section of net) with a border rope possessing a minimum breaking strength of 5,000 pounds. 29 CFR 1926.502(c)(8).
Do not allow one weak link to compromise a safety net. Use connections between safety net panels that are as strong as integral net components and spaced no more than 6 inches apart. 29 CFR 1926.502(c)(9).
Fall Protection Systems I
Notes: 1926.502(c)"Safety net systems." Safety net systems and their use shall comply with the following provisions:
1926.502(c)(1)Safety nets shall be installed as close as practicable under the walking/working surface on which employees are working, but in no case more than 30 feet (9.1 m) below such level. When nets are used on bridges, the potential fall area from the walking/working surface to the net shall be unobstructed.
1926.502(c)(2)Safety nets shall extend outward from the outermost projection of the work surface as follows:
____________________________________________________________________ | Vertical distance from working | Minimum required horizontal level to horizontal plane |distance of outer edge of net of net | from the edge of the working | surface _____________________________________|_____________________________ | Up to 5 feet ........................| 8 feet. More than 5 feet up to 10 feet ......| 10 feet. More than 10 feet ...................| 13 feet. _____________________________________|_____________________________
1926.502(c)(3)Safety nets shall be installed with sufficient clearance under them to prevent contact with the surface or structures below when subjected to an impact force equal to the drop test specified in paragraph (c)(4) of this section.
1926.502(c)(4)Safety nets and their installations shall be capable of absorbing an impact force equal to that produced by the drop test specified in paragraph (c)(4)(i) of this section.
1926.502(c)(4)(i)Except as provided in paragraph (c)(4)(ii) of this section, safety nets and safety net installations shall be drop-tested at the jobsite after initial installation and before being used as a fall protection system, whenever relocated, after major repair, and at 6-month intervals if left in one place. The drop-test shall consist of a 400 pound (180 kg) bag of sand 30 + or - 2 inches (76 + or - 5 cm) in diameter dropped into the net from the highest walking/working surface at which employees are exposed to fall hazards, but not from less than 42 inches (1.1 m) above that level.
1926.502(c)(4)(ii)When the employer can demonstrate that it is unreasonable to perform the drop-test required by paragraph (c)(4)(i) of this section, the employer (or a designated competent person) shall certify that the net and net installation is in compliance with the provisions of paragraphs (c)(3) and (c)(4)(i) of this section by preparing a certification record prior to the net being used as a fall protection system. The certification record must include an identification of the net and net installation for which the certification record is being prepared; the date that it was determined that the identified net and net installation were in compliance with paragraph (c)(3) of this section and the signature of the person making the determination and certification. The most recent certification record for each net and net installation shall be available at the jobsite for inspection.
1926.502(c)(5)Defective nets shall not be used. Safety nets shall be inspected at least once a week for wear, damage, and other deterioration. Defective components shall be removed from service. Safety nets shall also be inspected after any occurrence which could affect the integrity of the safety net system.
1926.502(c)(6)Materials, scrap pieces, equipment, and tools which have fallen into the safety net shall be removed as soon as possible from the net and at least before the next work shift.
1926.502(c)(7)The maximum size of each safety net mesh opening shall not exceed 36 square inches (230 cm) nor be longer than 6 inches (15 cm) on any side, and the opening, measured center-to-center of mesh ropes or webbing, shall not be longer than 6 inches (15 cm). All mesh crossings shall be secured to prevent enlargement of the mesh opening.
1926.502(c)(8)Each safety net (or section of it) shall have a border rope for webbing with a minimum breaking strength of 5,000 pounds (22.2 kN).
1926.502(c)(9)Connections between safety net panels shall be as strong as integral net components and shall be spaced not more than 6 inches (15 cm) apart.

## Slide 18: Fall Arrest System Design Factors
The purpose of a fall arrest system is to reduce the risk of injury from an accidental fall to an acceptable level.
The risk of injury from a fall can never be eliminated, only reduced.
How far a worker falls before shock absorbing or deceleration equipment begins to take effect
    Affects both impact forces and total fall distance
Fall Protection Systems I

## Slide 19: Primary Concerns 1
Impact Force to the Body Less Than 1800# (with a harness)
Maximum 6’ Free Fall Distance
May Not Hit Structures Below
Maximum Weight of Individual w/Tools of as rated by manufacturer
When fall arrest is used it must designed to be used 100% of the time.
Fall Protection Systems I

## Slide 20: Primary Concerns 2
How far will I fall before I am completely stopped?
What will I hit on the way down?
How will they get me down?
Fall Protection Systems I

## Slide 21: Personal Fall Arrest Systems (PFAS)
Connecting devices (Shock absorbing Lanyard with locking snap-hooks)
Body Wear (Full-body harness)
Anchorage Point / Tie-off Point
Fall Protection Systems I

## Slide 22: Anchorage Point 1
Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms.
Be capable of supporting at least 5,000 pounds per employee attached.
    3000 pounds when using fall restraint or a Self-Retracting Lifeline (SRL, Retractable, or “yo-yo”) which limits free fall distance from 2 – 4.5 feet
Shall be designed, installed, and used as follows:
    As part of a complete personal fall arrest system which maintains a safety factor of at least two; and
    Under the supervision of a qualified person.
Fall Protection Systems I
Notes: NOTE---HORIZONTAL LIFELINES---ONLY OPTION IS TWICE MAXIMUM ARRESTING FORCE – which will require some calculation, unless using a manufactured system in accordance with the manufacturers’ requirements
1926.502(d)(8)Horizontal lifelines shall be designed, installed, and used, under the supervision of a qualified person, as part of a complete personal fall arrest system, which maintains a safety factor of at least two.

## Slide 23: Anchorage Point 2
Must limit the fall distance to 6 feet before deceleration and harnesses must not exert more than 1,800 lbs. on body
ANSI requires no more then 900 lbs. of force on the body
Fall Protection Systems I
Notes: 1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:
1926.502(d)(9)Lanyards and vertical lifelines shall have a minimum breaking strength of 5,000 pounds (22.2 kN).

## Slide 24: Anchor Types 1
Peak Anchor (One or Two D-Rings)
Truss Anchor (including Spreaders)
I-beam clamp and structural steel (vertical or horizontal beams)
Trolley beam anchor
Standing seam metal roof anchor
Cable anchorage sling
Strap anchor (web)
Fall Protection Systems I

## Slide 25: Anchor Types 2
Concrete anchors
Bolt-on wall anchor
Rotating retractable anchor mast
Mobile fall protection system
Dead weight anchor
Fall Protection Systems I

## Slide 26: Anchor Types 3
Wood Beam Clamp
Pipe Clamp Anchor
Bolt on/in Anchors
Wrap-Around lanyards
Fall Protection Systems I

## Slide 27: Anchorage Point 3
What if I don’t have an identified anchorage point?
    Use a building structural beam
    What if I don’t know what force my anchorage point will hold?
    Minimize the arresting force
Engineers need time to do their work – pre-planning is key!
Fall Protection Systems I

## Slide 28: Connecting Devices (Lanyards) 1
Single Leg Lanyards
The most common type of shock absorber is a rip-stitch pouch that is attached integrally to a lanyard for fall arrest or a stitched lanyard.
Double Leg Lanyard
Recommend as an option to maintain 100% fall protection while moving where one lanyard is hooked at all times.
Fall Protection Systems I

## Slide 29: Connecting Devices (Lanyards) 2
Retractable Lifelines – Self Retracting Lifelines (SRLs)
Very effective for vertical applications.
Will normally lock up in 2 – 4.5 feet, minimizing total fall distance and impact forces on the worker’s body.
Fall Protection Systems I
Notes: 1926.502(d)(16)(v)have sufficient strength to withstand twice the potential impact energy of an employee free falling a distance of 6 feet (1.8 m), or the free fall distance permitted by the system, whichever is less. Note: If the personal fall arrest system meets the criteria and protocols contained in Appendix C to subpart M, and if the system is being used by an employee having a combined person and tool weight of less than 310 pounds (140 kg), the system will be considered to be in compliance with the provisions of paragraph (d)(16) of this section. If the system is used by an employee having a combined tool and body weight of 310 pounds (140 kg) or more, then the employer must appropriately modify the criteria and protocols of the Appendix to provide proper protection for such heavier weights, or the system will not be deemed to be in compliance with the requirements of paragraph (d)(16) of this section.

## Slide 30: Connecting Devices (Lanyards) 3
Workers who move away from retractables are subject to swing falls.
Retractables must be attached directly to the harness or a short D-ring extender
Self-retracting lifelines and lanyards that automatically limit free fall distance to 2 feet or less must be capable of sustaining a minimum tensile load of 3,000 pounds applied to the device with the lifeline or lanyard in the fully extended position.
Fall Indicator
Deployed
Fall Protection Systems I
Notes: 1926.502(d)(12)Self-retracting lifelines and lanyards which automatically limit free fall distance to 2 feet (0.61 m) or less shall be capable of sustaining a minimum tensile load of 3,000 pounds (13.3 kN) applied to the device with the lifeline or lanyard in the fully extended position.
1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:
1926.502(d)(15)(i)as part of a complete personal fall arrest system which maintains a safety factor of at least two; and
1926.502(d)(15)(ii)under the supervision of a qualified person.

## Slide 31: Safety Ropes 1
A rope grab fall arrester travels on a lifeline and will automatically engage the lifeline and lock to arrest an accidental fall of a person.
Used in vertical and in restraint systems.
The lanyard used with the rope grab fall arrester and vertical lifeline must be no longer than three (3) feet and should contain an energy-absorbing device.
Fall Protection Systems I

## Slide 32: Safety Ropes 2
Fall Protection Systems I

## Slide 33: Horizontal Lifelines 1
Horizontal lifelines require special attention during design and installation to:
    Limit the distance the worker can fall (a greater sag in the line can mean a farther fall);
    Minimize the forces on the connectors at the anchorage (a greater sag in the line can mean lower forces on the anchorage connectors at either end); and
    A qualified person must supervise the horizontal lifeline’s design, installation, and use.
Temporary
Permanent
Fall Protection Systems I
Notes: 502(d)(8) Shall be designed, installed, and used, under the supervision of a qualified person, as part of a complete personal fall arrest system, which maintains a safety factor of at least two.

## Slide 34: Horizontal Lifelines 2
Serve as anchoring lines that are rigged between fixed anchor points on the same level.
HLL designed to help minimize the potential for the dangerous “pendulum” like swing falls.
Should be positioned at a height above the waist.
Fall Protection Systems I

## Slide 35: Horizontal Lifelines 3
Depending on their geometry and sag angle, horizontal lifelines may be subjected to greater loads than the impact load imposed by an attached component.
When the horizontal lifeline’s sag is less than 30 degrees, the impact force imparted to the lifeline by an attached lanyard is greatly amplified.
    A 150 sag angle amplifies the force approximately 2:1.
    A 50 sag angle amplifies the force approximately 6:1.
Fall Protection Systems I

## Slide 36: Horizontal Lifelines 4
What are the hazards?
Swing Fall
Pendulum Effect
If not properly designed, you could hit the ground
Fall Protection Systems I

## Slide 37: Body (Harnesses) 1
Harness must be sized for the worker
Need to be inspected frequently (daily before use by the worker, at least monthly by a Competent Person)
Should never be modified
Should be taken out of service immediately if defective or exposed to an impact
Chest strap tightened at mid chest
Leg straps snug but not binding
Sub-pelvic (“Butt”) strap supports the load
“D” ring between shoulder blades
Fall Protection Systems I

## Slide 38: Body (Harnesses) 2
“Rules of Thumb”
    Be able to reach your D-ring with your thumb
    Maximum Four (flat) Fingers of Slack at the legs, straps as high as comfortably possible
    Ensure chest strap is across the chest/breastbone
    Have a buddy double check for twists, etc…
Fall Protection Systems I

## Slide 39: Personal Fall Arrest Systems (PFAS) 1
The purpose of a fall arrest system is to reduce the risk of injury from an accidental fall to an acceptable level.
    The risk of injury from a fall can never be eliminated, only reduced.
How far a worker falls before shock absorbing or deceleration equipment begins to take effect, affects both impact forces and total fall distance
Anchorage point location in relation to D-ring height
    Below the D-ring allows excessive falls
    Above the D-ring minimizes free fall to less than 6’
Fall Protection Systems I

## Slide 40: Foot Level Anchorage
6 foot lanyard
3 ½ foot deceleration distance
6 foot from attachment to feet
3 feet safety factor
23 ½ feet total
18 ½ feet off lower level
5 foot before D-ring passes anchorage point
Total 11’ travel distance of d-ring before fall arrest takes effect. This potential impact force exceeds many lanyard capacities (and OSHA standards).
All distances are approximate and shown for illustration only. This is why it is critical to maintain the safety factor distance!
Fall Protection Systems I

## Slide 41: Shoulder Level Anchorage
Fall Protection Systems I

## Slide 42: Overhead Anchorage
Fall Protection Systems I

## Slide 43: Personal Fall Arrest Systems (PFAS) 2
Even if you are using a fall arrest system, your body will not be braked at a uniform rate - certain parts will experience localized acceleration in relation to others.
The duration and distance of your deceleration, and the degree to which parts of your body are stressed, depends on many factors including
    Weight
    Distance you fall
    Characteristics of the fall arrest system
    Orientation of your body at the onset of deceleration
Fall Protection Systems I

## Slide 44: Fall Distance Exercise
These workers are tied to the beams they are standing on with choker slings.
How far will they fall?
Calculate free fall distance
Calculate total fall distance
Fall Protection Systems I

## Slide 45: Personal Fall Arrest Systems (PFAS) 3
Swing Fall
A
B
Obstructions
Fall Protection Systems I

## Slide 46: Fall Rescue 1
The Suspension Phase of a fall lasts until you are rescued (assuming that you cannot regain your footing without assistance).
You may be unconscious or incapacitated in some way.
Your tolerance for suspension without risk of serious or fatal injury is relatively short especially if you are not in peak physical condition. (15-20) minutes
    Orthostatic Intolerance will set in
Spread load across butt strap and belt strap if on the harness
Excess pressure here can cut blood flow to the legs
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 47: Fall Rescue Factors that can affect the degree of risk of suspension trauma:2
Inability to move legs | Hypothermia
Pain | Shock
Injuries during the Fall | Cardiovascular disease
Fatigue | Respiratory disease
Dehydration | Blood loss
References: Seddon, Paul. Harness Suspension: review and evaluation of existing information. Health and Safety Executive. Research Report 451/2002. 104 pp.
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves. There must be a plan to retrieve or rescue a fallen worker.
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 48: Fall Rescue 3
Rescue
    Self-Rescue - Primary
      With proper personal fall protection equipment, training and practice, a fallen worker can take steps to minimize suspension trauma. Self-rescue methods allow a fallen worker to temporarily relieve pressure on the legs or in some cases to even lower himself or herself to the lower level.
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 49: Fall Rescue 4
Rescue
    Aided Rescue - Secondary
      A worker who is suspended from a lifeline and cannot perform a self-rescue will need help from trained rescuers using appropriate equipment, including appropriate fall protection.
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 50: Fall Rescue 5
Rescue
    Professional Rescue – Last Option
      Off-site emergency response personnel may rescue suspended workers, although most 911 responders are not trained in how to do so.
      Time to respond?
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 51: Fall Rescue 6
When it works
Fall Protection Systems I
Notes: 1926.502(d)(20)
The employer shall provide for prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves.

## Slide 52: Questions?
Fall Protection Systems I