## Slide 1: Operations with Fall Hazards
Commercial Roofing
Fall Prevention in Construction

## Slide 2: Learning Objectives
Understand the difference between a low sloped roof and steep sloped roof
Understand the responsibilities of the safety monitor
Understand the requirements for warning line systems
Identify safe work practices while performing roofing work
Operations with Fall Hazards – Commercial Roofing

## Slide 3: Roofing Definitions
Roof
    means the exterior surface on the top of a building. This does not include floors or formwork which, because a building has not been completed, temporarily become the top surface of a building.
Roofing work
    means the hoisting, storage, application, and removal of roofing materials and equipment, including related insulation, sheet metal, and vapor barrier work, but not including the construction of the roof deck.
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.500(b) Definitions.

## Slide 4: Low slope vs. Steep slope
Low slope roof
    means a roof having a slope less than or equal to 4 in 12 (vertical to horizontal).
Steep slope roof
    means a roof having a slope greater than 4 in 12 (vertical to horizontal).
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.500(b) Definitions

## Slide 5: Roofing Work on Low-slope Roofs
When engaged in roofing work on a low-slope roof that has one or more unprotected side or edge 6 feet or more above lower levels, workers must be protected from falling by:
    Guardrail systems,
    Safety net systems,
    Personal fall arrest systems,
    A combination of conventional fall protection systems and warning line systems, or
    A warning line system and a safety monitoring system.
    When engaged in roofing work on low-slope roofs 50 feet or less in width, the use of a safety monitoring system without a warning line system is permitted.
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.501(b)(10)

## Slide 6: Roofing Work on Steep-slope Roofs
When working on a steep roof that has one or more unprotected side or edge 6 feet or more above lower levels, each worker must be protected by:
    Guardrail systems with toeboards,
    Safety net systems, or
    Personal fall arrest systems.
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.501(b)(11)

## Slide 7: Parapet Walls
Parapet walls must be at least 39” high or roof fall protection must be provided.
Operations with Fall Hazards – Commercial Roofing

## Slide 8: Methods of Roof Fall Protection
Safety Monitors
Guardrails and warning lines
Fall Arrest or Restraint
Operations with Fall Hazards – Commercial Roofing

## Slide 9: No Fall Protection!!!
Operations with Fall Hazards – Commercial Roofing
Notes: Picture depicts 3 workers without proper fall protection

## Slide 10: High Flat Roofs
While warning lines and safety monitors are allowed by OSHA, guardrails or fall arrest or restraints are safer protections.
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.502(h)"Safety monitoring systems." Safety monitoring systems [See 1926.501(b)(10) and 1926.502(k)] and their use shall comply with the following provisions:
1926.502(h)(1)The employer shall designate a competent person to monitor the safety of other employees and the employer shall ensure that the safety monitor complies with the following requirements:
1926.502(h)(1)(i)The safety monitor shall be competent to recognize fall hazards;
1926.502(h)(1)(ii)The safety monitor shall warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;
1926.502(h)(1)(iii)The safety monitor shall be on the same walking/working surface and within visual sighting distance of the employee being monitored;
1926.502(h)(1)(iv)The safety monitor shall be close enough to communicate orally with the employee; and
1926.502(h)(1)(v)The safety monitor shall not have other responsibilities which could take the monitor's attention from the monitoring function.

## Slide 11: Weighted Portable Guardrails
Operations with Fall Hazards – Commercial Roofing

## Slide 12: Skylights 1
Must be protected
Operations with Fall Hazards – Commercial Roofing
Notes: Ideally, barricades prevent access to the skylights. If covers are provided, they must support twice the intended load.
The photo on the right is from a fatality investigation, where an employee sat on the skylight to eat his lunch and fell through.

## Slide 13: Skylights 2
Grates
Covers
Operations with Fall Hazards – Commercial Roofing

## Slide 14: Roof Hatches
Hatch entrances need to be protected if too close the roof edge.
Hatches should be considered holes when open.
Operations with Fall Hazards – Commercial Roofing

## Slide 15: Roof & Deck Anchors 1
Permanent
Anchors
Wood Roof
Anchor
Metal Roof
Anchor
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:

## Slide 16: Roof & Deck Anchors 2
Operations with Fall Hazards – Commercial Roofing
Notes: 1926.502(d)(15)Anchorages used for attachment of personal fall arrest equipment shall be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or shall be designed, installed, and used as follows:

## Slide 17: Questions?
Operations with Fall Hazards – Commercial Roofing