## Slide 1
Utilities Protection
Oct. 2021 – Sep. 2022
Trenching & Excavation Hazards in Construction
OSHA Susan Harwood Training Grant

## Slide 2
Review the Damages and Costs of Utility Strikes
Responsibilities of Excavators working around Utilities.
Use of the State Utility Locating Services, Clearance requirements and 811Contact
Methods of Locating, Marking Utilities & Protection of Utilities during Excavation
Reporting and Responding to a Utility Strike
Learning Objectives
Utilities Protection

## Slide 3
Utility Strikes
Utilities Protection
Water Main Strikes
Telecommunications Strike
High pressure Gas Line Strikes
Notes: Ensuring that everyone is working safely around underground facilities is key to damage prevention. Below, we outlined some of the main factors to consider when working near each type of utility and what to do if a damage occurs. It is important to keep yourself and your crew safe so that everyone can go home at the end of the day.
GENERAL SAFETY AT THE WORKSITE:
Always verify marking instructions before beginning your work by using a copy of the Locate Ticket to confirm the markings are correct and match the ticket.
Take photos or video to document the markings before you start to dig.
Do NOT excavate outside your requested area of work.
If you are going to dig outside of the marking instructions, you MUST call Diggers Hotline for a new locate request that will cover the expanded dig area.
Never assume a site is clear if you see no marks. Above ground indicators can give clues as to what may not have been marked at a job site.
Contact your local utility or utility locator with any questions or concerns of confusing or missing locate markings. It is always a good idea to request additional information if the markings are not clear.
NATURAL GAS & PETROLEUM PIPELINES:
Transmission pipeline companies generally require a company representative to be on site when digging near a pipeline. This is referred to as a Watchdog or Standby.
The facility owner MUST be notified any time it’s suspected that damage has occurred to a facility. It’s the law. Even something as minor as a dent or scratch can cause facility failure down the road.
If contact has been made with a natural gas or flammable liquids facility, be familiar with the warning signs of a leak, which include:
Smelling like rotten eggs or oil. Keep in mind that natural gas transmission lines may not be odorized.
Hearing a hissing, blowing or roaring sound.
Seeing a white cloud or fog, water bubbling, discolored or dead vegetation, flames or vapors.
In the case of a petroleum product leak, you may see an oily sheen or a pool of liquid.
Remember that natural gas is lighter than air and will quickly dissipate into the atmosphere. Other petroleum products found in pipelines are heavier than air and will collect in low areas.
Even a minor hit can cause unexpected exposure and damage. With this in mind you should:
Always report any and all nicks, dents, scratches, or cut tracer wires.
Never stop a leak or attempt to fix a leak yourself. Static electricity on the pipe could cause ignition.
Never bury a leak because natural gas can migrate underground and find a remote ignition source
Never operate any pipeline equipment, including turning valves. Turning a valve can cause problems up or down stream of your location.
If there is an escape of natural gas or flammable liquids you MUST do the following:
Eliminate all ignition sources by immediately turning off the equipment, cellphones, lighters, cars and trucks.
Immediately evacuate the area and stay up wind. Do not start any vehicles to leave the area as this could become an ignition source.
Call 911 from a safe location and notify the facility owner as soon as possible.
Utility company contact information can be found on pipeline marker posts located along roadways.
The contractor is responsible for securing the area and ensuring the safety of the crew and public, until emergency responders arrive.
ELECTRIC LINES:
Treat all downed lines like they are live. Insulation may contain pinholes or flaws that can cause shocks.
When a line flashes and stops, it does not mean it is de-energized. Lines can become re-energized at any time.
If a piece of equipment comes in contact with an energized facility while the operator is on it, it is recommended that the operator try to remove the machine or equipment. Only do this if it can be safely disengaged without causing additional damage or risking injury or death.
If the equipment cannot be safely removed from the energized cable, you must stay on the equipment. You are energized, but safe like a bird on a wire.
Call the Electric Utility immediately to get the current turned off.
Warn others to stay away from the area as the ground and equipment are energized.
If you are unable to stay on the equipment due to fire:
Jump clear of the equipment, making sure to land with both feet together, and never touching both the equipment and the ground at the same time.
Shuffle away keeping the feet together. Never go further than toe-to-heel apart.
Doing this will keep you from being in more than one voltage ring at a time and avoid electrocution.
FIBER OPTICS & COMMUNICATION LINES:
Communications lines can be buried just below the surface. Never assume they are deeper than you are digging.
Damages to communication lines can take out cellphone and 911 service along with internet connections.
Immediately report any damaged lines to the facility owner so they can initiate the repair process.
The cost to repair a fiber optic line is much greater than repairing other communications lines. Many times they cannot be repaired and must be replaced.
Fiber optic lines are becoming more popular, especially in rural areas and with home businesses. Damages can cause costly delays in work, not only for you and your crew, but also business owners. The cost of repairs and any 3rd party claims add to the total cost of the damage.
Never look into the end of a damaged fiber optic line. Laser lights can cause eye injury.
WATER & SEWER LINES:
Water under pressure can cause serious injury.
Just slight damage to high-pressure water lines, like shovel scratches or nicks, can cause pipeline breaks.
Wastewater contains bacteria that can be a significant health risk.
Sewer gas is flammable. Avoid open flames and other ignition sources.
Do not close valves to stop the flooding. Closing the wrong valve can affect fire flows.
Still looking for more?

## Slide 4
Damages are on the rise. The number of damage reports reached an all-time high of 453,766
For 2019 alone, the societal costs of damages to buried utilities in the U.S. is estimated at $30 billion.
This estimate accounts for direct costs (facility repair) and indirect costs (property damage, medical bills, businesses unable to operate, etc.).
Damages in 2019
Utilities Protection
The DIRT Report 2019 – CGA
(DIRT - Damage Information and Reporting Tool)
Notes: Damages are the Costs of Repairing Utility Lines and also other Damages such as Lost Service Outages, Damage to adjacent Facilities, Business Downtime, etc.
Damages in 2019
· Damages are on the rise. The number of damage reports entered in DIRT, both before and after applying the method to match and weight multiple reports of the same event, reached an all-time high at 534,151 and 453,766 respectively.
· The estimate of total damages in the U.S. increased 4.5% year-over-year to 532,000, mirroring a 4.5% increase in damages per million dollars of construction spending. Interestingly, the number of transmissions per every construction dollar spent rose in 2019 – a potential indicator of stress on the damage prevention system.
· Enhancements in the quality of DIRT submissions could substantially increase the strength of the DIRT Report and the resulting recommendations.
Enormous Societal Costs of Damages
· For 2019 alone, the societal costs of damages to buried utilities in the U.S. is estimated at $30 billion. This estimate accounts for direct costs (facility repair) and indirect costs (property damage, medical bills, businesses unable to operate, etc.). All stakeholders have a clear interest in reducing damages to buried utilities as a means of reducing these enormous societal costs.
Root Cause Analysis
· Failure to notify the one call center/811 (No Locate Request) remains the largest individual damage root cause, but the root cause groupings of Excavation Issues, Locating Issues, and Invalid Use of Locate Request all appear roughly equal, suggesting that improvements are needed in every step of the safe excavation process in order to reverse the damage trend.
· Distinguishing between damage liability and true damage root cause when submitting to DIRT would better illustrate where behavior changes could result in improved safety outcomes.
Reexamining Best Practices
· The biggest categories of damage root causes correspond to Best Practices that lack specificity, likely reflecting the difficulty of achieving consensus among all 16 CGA stakeholder groups, which is required by the Best Practices process.
· With low-hanging fruit harvested, the remaining issues facing the industry are more challenging ones. Still, the 2019 DIRT Report includes recommendations for reexamining key Best Practices to combat the largest drivers of damages to buried utilities.
Interactive Dashboard
· Explore the 2019 (and 2018) DIRT data using the Interactive Dashboard, which allows users to apply a range of filters to create custom data views.
COMMON GROUND ALLIANCE 2

## Slide 5
Damages by Facility Operation
Utilities Protection
Notes: Table 2 shows the leading event source for each type of facility damaged. The self-reporting columns indicate the level to which the corresponding event source (where applicable) submits DIRT reports. Liquid pipe and natural gas are the only ones with self-reporting as the leading source. They are less than 50% self-reporting because other sources such as locators, excavators and regulators also enter DIRT reports for those facilities.
https://commongroundalliance.com/Publications-Media/DIRT-Report/2019-DIRT-Report

## Slide 6
Damage Root Cause Groups
Utilities Protection
Notes: Figure 5 shows the major root cause groupings for 2015 through 2019, excluding unknown root causes. The DIRT root causes were revamped starting in 2018. Prior to that, abandoned facilities were grouped with Miscellaneous root causes. Abandoned facilities are now grouped with Locating Practices and are presented that way in Figure 5 for the entire graph. Moving abandoned facilities out of the Miscellaneous group leaves the total for the remaining Miscellaneous root causes negligible, and they are also filtered out of Figure 5. The revamping also contributed to the decrease in Excavating Practices and roughly corresponding increase in Invalid Use of Request at the 2017-2018 transition.6 With these adjustments, Figure 5 allows us to visualize trends in root cause groups over the past five years. In 2019, the No Locate Request, Excavating Practices and Locating Practices root cause groupings are converging toward approximately equal, with the impact of Invalid Use of Request also becoming more focused.

## Slide 7
Top 10 Reported Damages by Root Cause 2019 – Dirt Report CGA
Utilities Protection
Notes: 2019 DIRT REPORT
Examining Root Causes
The main DIRT root cause groups are equalizing in terms of their contributions to the total number of damages, indicating that systematic improvements need to occur across the damage prevention process.
It is important to distinguish between damage liability and true damage root causes in order to accurately identify where changes in behavior could lead to changes in outcomes.
Failing to notify the one call center (No Locate Request) remains the single largest individual root cause of damages at 29.1%, followed by excavator failing to maintain clearance (16.7%) and facility marked inaccurately due to locator error (10.6%).
Root Cause by Group
Table 4— Reported damages by root cause for 2019 (color coded by root cause group) The Data Committee sorts these 26 individual root causes into 6 groups to provide a high-level snapshot of what went wrong in the damage prevention process.
COMMON GROUND ALLIANCE 12

## Slide 8
Utility locating should be addressed early in a project planning process.
ALL utilities must be properly located and marked before any excavation begins.
Utilities may need to be relocated to allow the excavation work to be performed.
Plans to support vulnerable utilities must be established before excavation begins.
Planning
Utilities Protection
Notes: 1926.651(b)
Underground installations.
1926.651(b)(1)
The estimated location of utility installations, such as sewer, telephone, fuel, electric, water lines, or any other underground installations that reasonably may be expected to be encountered during excavation work, shall be determined prior to opening an excavation.
1926.651(b)(2)
Utility companies or owners shall be contacted within established or customary local response times, advised of the proposed work, and asked to establish the location of the utility underground installations prior to the start of actual excavation. When utility companies or owners cannot respond to a request to locate underground utility installations within 24 hours (unless a longer period is required by state or local law), or cannot establish the exact location of these installations, the employer may proceed, provided the employer does so with caution, and provided detection equipment or other acceptable means to locate utility installations are used.
1926.651(b)(3)
When excavation operations approach the estimated location of underground installations, the exact location of the installations shall be determined by safe and acceptable means.
1926.651(b)(4)
While the excavation is open, underground installations shall be protected, supported or removed as necessary to safeguard employees.

## Slide 9
All One-Call Centers can be reached through the center’s toll-free number, e-mail or by dialing 811.
One Call System requirements are set by each State.
The “One Call Center is a “clearinghouse”
The utility owner is responsible for marking the underground utilities either with their own employees or a contract locator service.
Locates and 811 Laws
Utilities Protection
Notes: 1926.651(b)(2)
Utility companies or owners shall be contacted within established or customary local response times, advised of the proposed work, and asked to establish the location of the utility underground installations prior to the start of actual excavation. When utility companies or owners cannot respond to a request to locate underground utility installations within 24 hours (unless a longer period is required by state or local law), or cannot establish the exact location of these installations, the employer may proceed, provided the employer does so with caution, and provided detection equipment or other acceptable means to locate utility installations are used.

## Slide 10
Each State Has a One-Call Center
Utilities Protection

## Slide 11
The actual entity that will do the excavation must request and maintain the locate ticket.
One contractor may not dig on another contractor’s ticket.
Failure of the right entity (the excavator) to have a valid ticket number could lead to potential liability issues in the event of damage to a utility.
Locate Request Responsibility
Utilities Protection
Notes: 1926.651(b)(2)
Utility companies or owners shall be contacted within established or customary local response times, advised of the proposed work, and asked to establish the location of the utility underground installations prior to the start of actual excavation. When utility companies or owners cannot respond to a request to locate underground utility installations within 24 hours (unless a longer period is required by state or local law), or cannot establish the exact location of these installations, the employer may proceed, provided the employer does so with caution, and provided detection equipment or other acceptable means to locate utility installations are used.

## Slide 12
The locate request is dispatched from the One-Call Center to all utilities shown in the locate area.
Utilities, or their locating contractor, mark facilities according to specific State guidelines and color codes.
Utility Locating
Utilities Protection

## Slide 13
Private utilities on private property may not be included
It may the responsibility of the property owner to locate those facilities.
Private Utilities
Utilities Protection

## Slide 14
Electric – HV power, LV power like light circuits.
Gas – Natural gas, propane, liquid fuels, etc,
Communication – Phone, data, fiber-optics
Water – Mains, secondary low pressure, etc.
Sewer – Sanitary, drainage, etc.
Type of Utilities Found
Universal Color Coding
Utilities Protection

## Slide 15
Utility Marking
Utilities Protection

## Slide 16
It is good practice to photograph the marking.
This is valuable in case of any issues
Documentation
Utilities Protection
Notes: Always verify marking instructions before beginning your work by using a copy of the Locate Ticket to confirm the markings are correct and match the ticket.
Take photos or video to document the markings before you start to dig.
Do NOT excavate outside your requested area of work.
If you are going to dig outside of the marking instructions, you MUST call Diggers Hotline for a new locate request that will cover the expanded dig area.
Never assume a site is clear if you see no marks. Above ground indicators can give clues as to what may not have been marked at a job site.
Contact your local utility or utility locator with any questions or concerns of confusing or missing locate markings. It is always a good idea to request additional information if the markings are not clear.

## Slide 17
The State marking requirements may not give a specific maximum distance that markings must be from a marked utility.
This is particularly important because locating is not an exact science and, therefore, the actual location of the facility could vary from the position of the marks.
Always be aware that the utility may be off the marks.
The physical location of the utility must be determined by probing, hand excavation etc. using the marks as a reference.
Locating and Marking
Utilities Protection
Notes: 1926.651(b)(3)
When excavation operations approach the estimated location of underground installations, the exact location of the installations shall be determined by safe and acceptable means.

## Slide 18
The excavator has the responsibility to physically locate the utility using marks as references.
Probing
Hand Excavation
Physically Locate the Utility
Utilities Protection
Probing with a long probe rod
Hand Digging with a shovel, spade, etc.
Notes: 1926.651(b)(3)
When excavation operations approach the estimated location of underground installations, the exact location of the installations shall be determined by safe and acceptable means.

## Slide 19
Using vacuum excavators has become a very efficient way of doing non-destructive physical locates.
Vacuuming relies on high pressure water to break up soil which is then vacuumed out of the probe hole.
Vacuum Probing & Pot Holing
Utilities Protection
Notes: This is less destructive to hand digging with shovels
When potholing, utility crews use a portable vacuum excavator. First, test holes, usually measuring 6 to 12 inches deep, are made along the line where they plan to dig or begin construction. They excavate soil with high-speed suction straight down until the utility line is partially uncovered.
Both air and hydro vacuum excavation can be used for potholing. These methods utilize pressurized water or air to quickly move ground contents out of the way. This allows operators to have a clear view of subsurface features.
Hydro and air vacuum excavation safely dig even through hard, compacted dirt, rocky soil, and clay. Unlike the traditional methods of using a shovel or heavy equipment, it won’t cut a utility line hidden below the surface. Vacuum excavation is a non-invasive, non-mechanical, and non-destructive process. Potholing with vacuum excavation simply uncovers the line, leaving it intact, without damaging or moving it. Plus, when compared to these other methods, vacuum excavation leaves a smaller site footprint and decreases the time needed to finish the job.
Then, displaced dirt and rock debris is suctioned away from the excavation area through a large hose. It is stored in a holding tank on the truck. Excavator trucks with different capacity tanks can be used to fit the size of the job. Once the lines have been accurately located, accumulated wet or dry soil which was removed during the digging process can be replaced as backfill.

## Slide 20
Excavators are required to maintain a minimum clearance between a marked and unexposed utility and the cutting edge or point of any power-operated excavating or earth-moving equipment.
The minimum clearance varies by State. (Approx. 18” – 36”)
If excavation with mechanical equipment is required within the State mandated minimum clearance the excavation should be performed very carefully with hand tools or the utility must first be exposed.
Clearance Requirements
Utilities Protection

## Slide 21
Examples – Clearance are from the outside of the utility
Clearances
Utilities Protection

## Slide 22
Utilities must be protected and supported if there is any possibility of damage to that utility.
Supporting Exposed Utilities
Utilities Protection
Notes: 1926.651(b)(4)
While the excavation is open, underground installations shall be protected, supported or removed as necessary to safeguard employees.

## Slide 23
If, a facility has been exposed, it is the excavator’s responsibility to inspect and support these facilities.
If damage of any kind is discovered or any suspicion of damage exists, it is the excavator’s responsibility to immediately notify the facility owner directly.
Damaged utilities should not be backfilled until the utility has inspected, repaired and approved backfilling
Securing, bracing, and protecting
Utilities Protection

## Slide 24
Shut down equipment and eliminate all potential ignition sources.
Contact 911 IMMEDIATELY
Call the Gas Company IMMEDIATELY
Everyone should evacuate the area and protect the area from others until emergency personnel arrive and the gas company.
Ruptured Gas Lines
Utilities Protection
Notes: If there is an escape of natural gas or flammable liquids you MUST do the following:
Eliminate all ignition sources by immediately turning off the equipment, cellphones, lighters, cars and trucks.
Immediately evacuate the area and stay up wind. Do not start any vehicles to leave the area as this could become an ignition source.
NATURAL GAS & PETROLEUM PIPELINES:
Transmission pipeline companies generally require a company representative to be on site when digging near a pipeline. This is referred to as a Watchdog or Standby.
The facility owner MUST be notified any time it’s suspected that damage has occurred to a facility. It’s the law. Even something as minor as a dent or scratch can cause facility failure down the road.
If contact has been made with a natural gas or flammable liquids facility, be familiar with the warning signs of a leak, which include:
Smelling like rotten eggs or oil. Keep in mind that natural gas transmission lines may not be odorized.
Hearing a hissing, blowing or roaring sound.
Seeing a white cloud or fog, water bubbling, discolored or dead vegetation, flames or vapors.
In the case of a petroleum product leak, you may see an oily sheen or a pool of liquid.
Remember that natural gas is lighter than air and will quickly dissipate into the atmosphere. Other petroleum products found in pipelines are heavier than air and will collect in low areas.
Even a minor hit can cause unexpected exposure and damage. With this in mind you should:
Always report any and all nicks, dents, scratches, or cut tracer wires.
Never stop a leak or attempt to fix a leak yourself. Static electricity on the pipe could cause ignition.
Never bury a leak because natural gas can migrate underground and find a remote ignition source
Never operate any pipeline equipment, including turning valves. Turning a valve can cause problems up or down stream of your location.Call 911 from a safe location and notify the facility owner as soon as possible.
Utility company contact information can be found on pipeline marker posts located along roadways.
The contractor is responsible for securing the area and ensuring the safety of the crew and public, until emergency responders arrive.

## Slide 25
No marking by One-Call.
All excavation equipment must maintain at least a 10-foot minimum clearance from all over head power lines less than 50 kV.
Additional clearance is required for power lines over 50 kV.
NOTE : Clearance for cranes may be greater
Overhead Power Lines
Utilities Protection

## Slide 26
“Underground utility safety and damage prevention is a shared responsibility. Owner/operators, locators, 811 centers, contractors, regulatory agencies and others have grave responsibilities in the process.
Without each stakeholder executing their responsibilities the process is compromised, endangering public and workforce safety, property, vital services, life and limb.”
Remember
Elements of an Effective Underground Utility Excavation Safety and Damage Prevention Program
AGC of America
Utilities Protection

## Slide 27
Questions?
Utilities Protection