## Slide 1
Protective Systems
Oct. 2021 – Sep. 2022
Trenching & Excavation Hazards in Construction
OSHA Susan Harwood Training Grant

## Slide 2
Understand Sloping and Benching based on Classification of Soils
Use of Trench Boxes and Other Protections
Access in and out of Excavations
Fall protection Requirements around Excavations
Methods for Soil Backfilling
Learning Objectives
Protective Systems

## Slide 3
SLOPE or bench trench walls by cutting back the trench wall at an angle inclined away from the excavation.
SHORE trench walls by installing aluminum hydraulic or other types of supports to prevent soil movement.
SHIELD trench walls by using trench boxes or other types of supports to prevent soil cave-ins.
Protective Systems for Trenches
Protective Systems

## Slide 4
Sloping Angles
Stable Rock
  Vertical angle
  Type A
    3/4 Horiz. to 1 Vert. (53 degree)
  Type B
    1 Horiz. to 1 Vert. (45 degree)
  Type C
    1-1/2 Horiz. to 1 Vert. (34 degree)
Protective Systems
Notes: 1926.652(b)
Design of sloping and benching systems. The slopes and configurations of sloping and benching systems shall be selected and constructed by the employer or his designee and shall be in accordance with the requirements of paragraph (b)(1); or, in the alternative, paragraph (b)(2); or, in the alternative, paragraph (b)(3), or, in the alternative, paragraph (b)(4), as follows:
1926.652(b)(1)
Option (1)-Allowable configurations and slopes
1926.652(b)(1)(i)
Excavations shall be sloped at an angle not steeper than one and one-half horizontal to one vertical (34 degrees measured from the horizontal), unless the employer uses one of the other options listed below.
1926.652(b)(1)(ii)
Slopes specified in paragraph (b)(1)(i) of this section, shall be excavated to form configurations that are in accordance with the slopes shown for Type C soil in appendix B to this subpart.
1926.652(b)(2)
Option (2)-Determination of slopes and configurations using Appendices A and B. Maximum allowable slopes, and allowable configurations for sloping and benching systems, shall be determined in accordance with the conditions and requirements set forth in appendices A and B to this subpart.

## Slide 5
Type “A” Sloping (1V:1/2H) Short Term (24 hours or less)
Simple Slope
Benched
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 6
Type “A” Sloping (3/4H:1V) Long Term (More than 24 hours)
Simple
Slope
Multiple Bench
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 7
Type “B” Sloping (1H:1V)
Simple
Slope
Multiple Bench
(Cohesive Soil Only)
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 8
Benching Examples
Protective Systems
Notes: Benching can also catch any loose soil particles or rocks that may come loose.

## Slide 9
Type “C” Sloping (1 -1/2H:1V)
Benching is not allowed.
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 10
Type B over Type A
Compound Soils
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 11
Sample Sloping Guide
Protective Systems
Notes: This a commercial slope guide to check slopes. Some contractors will provide a slope image to an operator that he/she can see through there lower excavator window.

## Slide 12
Trench Shields or Boxes
Engineered for all Types of soils.
Can be used with all classes of soils.
Shields can be stacked if allowed by manufacturer
Protective Systems
Notes: 1926.652(c)(2)(i)
Design of support systems, shield systems, or other protective systems that are drawn from manufacturer's tabulated data shall be in accordance with all specifications, recommendations, and limitations issued or made by the manufacturer.

## Slide 13
Light-weight, easy-to-assemble boxes.
Portable Trench Boxes
Protective Systems
Notes: Numerous types of light weight, portable trench boxes are now available for small project use.

## Slide 14
Trench Shield Placement
Shield in a Type B soil protecting only the bottom of the trench.
Protection must stick up at least 18 inches above soil
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 15
Trench boxes must protect full depth to within 2 feet of the bottom of the trench.
Trench boxes cannot be set on ledges.
Protective Systems
Notes: Shield systems-
1926.652(g)(1)
General.
1926.652(g)(1)(i)
Shield systems shall not be subjected to loads exceeding those which the system was designed to withstand.
1926.652(g)(1)(ii)
Shields shall be installed in a manner to restrict lateral or other hazardous movement of the shield in the event of the application of sudden lateral loads.
1926.652(g)(1)(iii)
Employees shall be protected from the hazard of cave-ins when entering or exiting the areas protected by shields.
1926.652(g)(1)(iv)
Employees shall not be allowed in shields when shields are being installed, removed, or moved vertically.
1926.652(g)(2)
Additional requirement for shield systems used in trench excavations. Excavations of earth material to a level not greater than 2 feet (.61 m) below the bottom of a shield shall be permitted, but only if the shield is designed to resist the forces calculated for the full depth of the trench, and there are no indications while the trench is open of a possible loss of soil from behind or below the bottom of the shield.

## Slide 16
Rigging must be checked, inspected and capable of handling the loads.
Excavators or other lifting machines must be working within their lifting capacities.
Lifting Trench Shields
Protective Systems
Notes: Engineering tables must be available for review. Sometimes the biggest lifts an excavator will make is actually the trench box. You must make sure that the excavator is not overloaded.
Also, hollow sided boxes may gain weight over time if water becomes trapped in the side walls.

## Slide 17
Boxes set tight to each other
Boxes sticking up 18 inches
Trench Box Sets
Protective Systems

## Slide 18
When surcharge loads from stored material or equipment, operating equipment, or traffic are present, a competent person shall determine the degree to which the actual slope must be reduced below the maximum allowable slope.
Soil Overloads
Protective Systems
Notes: (3) Actual slope. (i) The actual slope shall not be steeper than the maximum allowable slope.
(ii) The actual slope shall be less steep than the maximum allowable slope, when there are signs of distress. If that situation occurs, the slope shall be cut back to an actual slope which is at least ½ horizontal to one vertical (½H:1V) less steep than the maximum allowable slope.
(iii) When surcharge loads from stored material or equipment, operating equipment, or traffic are present, a competent person shall determine the degree to which the actual slope must be reduced below the maximum allowable slope, and shall assure that such reduction is achieved. Surcharge loads from adjacent structures shall be evaluated in accordance with § 1926.651(i).

## Slide 19
When stacking boxes user must assure that they use boxes that are designed the depth of the stacked boxes based on the soil type.
Stacking Trench Boxes
Protective Systems
Notes: Beading welding the maximum depth requirements may be a good way to always know the maximum depth.

## Slide 20
Hazards such as loose soil may cause a ground failure outside the box that could reach into the end of the box.
This must be addressed to protect workers from being struck by material that could enter into the box from the end.
Hazards Outside the Shoring
Protective Systems

## Slide 21
Excavation Access
Required in excavations over 4 feet deep.
Must be able to walk out without use of hands.
Provided with less than 25 feet of travel or every 50 feet.
Protective Systems
Notes: 1926.651(c)(2)
Means of egress from trench excavations. A stairway, ladder, ramp or other safe means of egress shall be located in trench excavations that are 4 feet (1.22 m) or more in depth so as to require no more than 25 feet (7.62 m) of lateral travel for employees.

## Slide 22
Access from ground to top of box must be protected with railings where a fall hazard exists.
Ladders must be secured.
Access to Trench Shields
Protective Systems
Notes: 1926.651(l)
Walkways shall be provided where employees or equipment are required or permitted to cross over excavations. Guardrails which comply with §1926.502(b) shall be provided where walkways are 6 feet (1.8 m) or more above lower levels.

## Slide 23
Falls into trench boxes or other vertical shoring must be protected.
Guardrails are a safe method of fall protection into excavations.
Fall Protection Around Trench Shields
Protective Systems
Notes: Guardrails should be used anytime someone can fall into the box. This comes for 1926.5091(b) related to falls into excavations and pits.

## Slide 24
Bridges should used when crossing a trench is required.
Bridges must have adequate fall protection such as guardrails
Crossing Over Trenches
Protective Systems
Notes: 1926.651(l)
Walkways shall be provided where employees or equipment are required or permitted to cross over excavations. Guardrails which comply with §1926.502(b) shall be provided where walkways are 6 feet (1.8 m) or more above lower levels.
All bridges must have guardrails if the excavation depth is more than 6 feet

## Slide 25
Timber shoring is an old for of protection.
Use of timber shoring requires great expertise to properly size the various members.
Installation of timber shoring must be done in a way that workers are not exposed to the cave-ins.
Timber Shoring
Protective Systems
Notes: Standard Number: 1926 Subpart P App C
Title: Timber Shoring for Trenches
GPO Source:e-CFR
(a) Scope. This appendix contains information that can be used when timber shoring is provided as a method of protection from cave-ins in trenches that do not exceed 20 feet (6.1 m) in depth. This appendix must be used when design of timber shoring protective systems is to be performed in accordance with 1926.652(c)(1). Other timber shoring configurations; other systems of support such as hydraulic and pneumatic systems; and other protective systems such as sloping, benching, shielding, and freezing systems must be designed in accordance with the requirements set forth in 1926.652(b) and 1926.652(c).

## Slide 26
OSHA provides Tables for Timber Shoring in Subpart P Appendix C.
Minimum sizes of members are specified for use in different types of soil.
The selection is based on the depth and width of the trench where the members are to be installed.
Use of Tables in Timber Shoring
Protective Systems
Notes: (e) Use of Tables. The members of the shoring system that are to be selected using this information are the cross braces, the uprights, and the wales, where wales are required. Minimum sizes of members are specified for use in different types of soil. There are six tables of information, two for each soil type. The soil type must first be determined in accordance with the soil classification system described in appendix A to subpart P of part 1926. Using the appropriate table, the selection of the size and spacing of the members is then made. The selection is based on the depth and width of the trench where the members are to be installed and, in most instances, the selection is also based on the horizontal spacing of the crossbraces. Instances where a choice of horizontal spacing of crossbracing is available, the horizontal spacing of the crossbraces must be chosen by the user before the size of any member can be determined. When the soil type, the width and depth of the trench, and the horizontal spacing of the crossbraces are known, the size and vertical spacing of the crossbraces are known, the size and vertical spacing of the crossbraces, the size and vertical spacing of the wales, and the size and horizontal spacing of the uprights can be read from the appropriate table.

## Slide 27
Manufactured systems must be installed in accordance with manufacturers instructions or from information provided in Subpart P Appendix
Hydraulic Shoring
Protective Systems
Notes: Drawings from OSGA Subpart P Appendix

## Slide 28
Manufactured Hydraulic Shoring
Protective Systems
Notes: Shoring tables are available hydraulic shoring systems from the manufacturer or tables are available in the OSHA

## Slide 29
Engineered Shoring
OSHA requires support systems to be designed and that the designs are available on site.
Protective Systems
Notes: These designs would normally be done by an engineer

## Slide 30
These piling shoring systems failing and were not properly engineered
Poorly Designed Shoring
Protective Systems
Notes: Dried out clay soul is breaking away between the pipe piles on the left.
On right the sheet pile is tipping into the excavation probably due to a lack of pile penetration into soil.

## Slide 31
These shoring systems must be fully engineered
Large Excavation Shoring Systems
Drilled Caison and driven H-pile system
Rebar tie, anchored and shotcreted system
Protective Systems
Notes: These types of shoring retentions systems are fully engineered systems that are installed under the review of the engineer.

## Slide 32
H-pile and timber lagging system
Protective Systems
Notes: In these systems H-piles are driven before excavation. Then as the excavation is dug down, lagging is installed between the H-piles as they are exposed.

## Slide 33
Spoil Piles must always be maintained at least 2 feet away from the top of the excavation
Spoil Piles
Protective Systems
Notes: This is to keep the weight of the soil away from the top of the trench and also to keep material rolling down the pile from entering the trench.

## Slide 34
Sometimes workers using portable compactors may be exposed to hazards in excavations
Workers must be Protected when Compacting back filled soil.
Protective Systems

## Slide 35
Soil Compaction is best accomplished by compactors that do not require employees to enter the trenches.
Soil Compaction in Trenches
Protective Systems
Notes: Here hydraulic compactors are installed on the end of excavator booms. This keeps workers from having to enter an excavation to compact the soil.

## Slide 36
Remote compactors are a safe method for compacting soils
Remote Control Compactors
Protective Systems
Notes: Here a remote-control compacting machine is utilized.

## Slide 37
Excavations that are not readily visible or can cause a hazard to people, traffic, etc. must be barricaded
Barricading Excavations
Protective Systems
Notes: This required under OSHA 1026.501(b) related to falls into excavations

## Slide 38
Protective Systems

## Slide 39
Questions?
Protective Systems