## Slide 1
Hazards
Oct. 2021 – Sep. 2022
Excavation & Trenching
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Hazards associated with Excavation & Trenching.
Methods suggested to identify and control hazards.
Best practices and suggestions in documenting all inspections for hazards.
Learning Objectives
Hazards

## Slide 3
Cave Ins, Caught In Between/Engulfment
Hazards
Notes: “Caught in-between” hazards kill workers in a variety of ways. These include: cave-ins and other hazards of excavation work; body parts pulled into unguarded machinery; standing within the swing radius of cranes and other construction equipment; caught between equipment & fixed objects.
Excavation hazards are common on construction sites. These workers are more than twice as likely to be killed as workers in any other type of construction work. Excavations and trenches are unstable by nature, and many types of serious hazards exist when doing this type of work.
Both photos show the result of an unprotected excavation and/or trench. The photo on the right show evidence of employees have been or about to working in the trench. The photo on the left shows a “Body Recovery Operation” stemming from a cave in in an unprotected excavation. The result of this accident was a worker fatality.

## Slide 4
Slope It
Shore It
Shield It
Stay Out Of It
Cave Ins, Caught In Between/Engulfment
Hazards
Notes: Trench collapses, or cave-ins, pose the greatest risk to workers' lives. To prevent cave-ins:
SLOPE or bench trench walls
SHORE trench walls with supports, or
SHIELD trench walls with trench boxes
STAY OUT of it
Employers should also ensure there is a safe way to enter and exit the trench. Keep materials away from the edge of the trench. Look for standing water or atmospheric hazards. Never enter a trench unless it has been properly inspected.

## Slide 5
Cave Ins, Caught In Between/Engulfment
Hazards
Notes: You must be protected from cave-ins because dirt will go wherever it wants to go.
This photo depicts what we call trench protection. While the crew was working inside the protection of the shield, they were unaffected from the large about of soil that broke away from the excavation wall and caved in.

## Slide 6
Cave Ins, Caught In Between/Engulfment
Hazards
Notes: 1926.652(a)(1)(ii)
Excavations are less than 5 feet (1.52m) in depth and examination of the ground by a competent person provides no indication of a potential cave-in
The competent person must remove workers from the excavation upon any evidence of a situation that could cause a cave-in (even if it under 5 ft in depth), such as accumulation of water in the trench or protective system problems. (The competent person must also take actions for other types of hazards such as falling loads or hazardous atmospheres.)
This photo show workers in a trench that is under 5 ft in depth that may not require some sort of protection from cave in we still have to be diligent for other hazardous situations. Access has to be maintained and also the competent person must inspect for hazardous issues.

## Slide 7
Subsurface Encumbrances include underground utilities, foundations, streams, water tables, transformer vaults, and geological anomalies.
Surface Encumbrances
Hazards
Notes: Subsurface Encumbrances include underground utilities, foundations, streams, water tables, transformer vaults, and geological anomalies.
1926.651(a)
Surface encumbrances. All surface encumbrances that are located so as to create a hazard to employees shall be removed or supported, as necessary, to safeguard employees.
The picture on the right illustrates the protection of the crossing utility while the photo on the left demonstrates the lack for protection of an object (loose rock/boulder) could injure or kill.

## Slide 8
Surface Encumbrances
Hazards
Notes: Photos indicate situations to avoid like things that could fall on you while you are in the trench or excavation. These photos also show that are certain situations that we face in the field may require engineering expertise in how to protect structures and utilities.

## Slide 9
Surface Encumbrances
Hazards
Notes: As you can see in the photo in the left some things cannot be anticipated such as wildlife or things that you uncover as you dig. With a good pre-planning you can be prepared and most of these hazards can be avoided.

## Slide 10
Adjacent Structures Stability refers to the stability of the foundation(s) of adjacent structures whose location may create surcharges, changes in soil conditions, or other disruptions that have the potential to extend into the failure zone of the excavation or trench.
Stability of Adjacent Structures
Hazards
Notes: Adjacent Structures Stability refers to the stability of the foundation(s) of adjacent structures whose location may create surcharges, changes in soil conditions, or other disruptions that have the potential to extend into the failure zone of the excavation or trench.
1926.651(i)
Stability of adjacent structures.
1926.651(i)(1)
Where the stability of adjoining buildings, walls, or other structures is endangered by excavation operations, support systems such as shoring, bracing, or underpinning shall be provided to ensure the stability of such structures for the protection of employees.
1926.651(i)(2)
Excavation below the level of the base or footing of any foundation or retaining wall that could be reasonably expected to pose a hazard to employees shall not be permitted except when:
1926.651(i)(2)(i)
A support system, such as underpinning, is provided to ensure the safety of employees and the stability of the structure; or
1926.651(i)(2)(ii)
The excavation is in stable rock; or
1926.651(i)(2)(iii)
A registered professional engineer has approved the determination that the structure is sufficently removed from the excavation so as to be unaffected by the excavation activity; or
1926.651(i)(2)(iv)
A registered professional engineer has approved the determination that such excavation work will not pose a hazard to employees.
1926.651(i)(3)
Sidewalks, pavements, and appurtenant structure shall not be undermined unless a support system or another method of protection is provided to protect employees from the possible collapse of such structures.

## Slide 11
Stability of Adjacent Structures
Hazards
Notes: A registered Professional Engineer (PE) needs to get involved early in these type of operations.
The photos depict situations that one may encounter during an excavation that may require the involvement of a registered Professional Engineer (PE). Structural analysis may be needed to determine additional measures require to provide stability for the structure and protection of the crew.

## Slide 12
Surface crossing of trenches should be discouraged; however, if trenches must be crossed, such crossings are permitted only under the following conditions:
Vehicle crossings must be designed by and installed under the supervision of a registered professional engineer.
Walkways or bridges must be provided for foot traffic. These structures shall:
    have a safety factor of 4;
    have a minimum clear width of 20 in (0.51 m);
    be fitted with standard rails; and
    extend a minimum of 24 in (.61 m) past the surface edge of the trench.
Surface Crossing of Trenches
Hazards
Notes: Surface crossing of trenches should be discouraged; however, if trenches must be crossed, such crossings are permitted only under the following conditions:
Vehicle crossings must be designed by and installed under the supervision of a registered professional engineer.
Walkways or bridges must be provided for foot traffic. These structures must:
  - have a safety factor of 4; this safety factor is the walkway/bridge can hold 4 times its intended load, like a scaffold.
  - have a minimum clear width of 20 inches (0.51 meters);
  - be fitted with standard rails; and
  - extend a minimum of 24 inches (0.61 meters) past the surface edge of the trench.

## Slide 13
Surface Crossing of Trenches
Hazards
Notes: Manufactured/Engineered systems are the best to use in most situations. Avoid just using what is just left around the project that may not be the best fit.

## Slide 14
Loose Rock and Soil Protection
Hazards
Notes: Temporary spoil must be placed no closer than 2 ft (0.61 m) from the surface edge of the excavation, measured from the nearest base of the spoil to the cut. This distance should not be measured from the crown of the spoil deposit. This distance requirement ensures that loose rock or soil from the temporary spoil will not fall on employees in the trench.
Spoil should be placed so that it channels rainwater and other run-off water away from the excavation. Spoil should be placed so that it cannot accidentally run, slide, or fall back into the excavation.
Permanent spoil should be placed at some distance from the excavation. Permanent spoil is often created where underpasses are built or utilities are buried. The improper placement of permanent spoil, i.e. insufficient distance from the working excavation, can cause an excavation to be out of compliance with the horizontal-to-vertical ratio requirement for a particular excavation. This can usually be determined through visual observation. Permanent spoil can change undisturbed soil to disturbed soil and dramatically alter slope requirements.
In these photos you can see that the spoil pile was not placed 2 feet away from edge of the excavation which now adds height of the pile to the depth of the trench.

## Slide 15
Loose Rock and Soil Protection
Hazards
Notes: Temporary spoil must be placed no closer than 2 ft (0.61 m) from the surface edge of the excavation, measured from the nearest base of the spoil to the cut. This distance should not be measured from the crown of the spoil deposit. This distance requirement ensures that loose rock or soil from the temporary spoil will not fall on employees in the trench.
Spoil should be placed so that it channels rainwater and other run-off water away from the excavation. Spoil should be placed so that it cannot accidentally run, slide, or fall back into the excavation.
Permanent spoil should be placed at some distance from the excavation. Permanent spoil is often created where underpasses are built or utilities are buried. The improper placement of permanent spoil, i.e. insufficient distance from the working excavation, can cause an excavation to be out of compliance with the horizontal-to-vertical ratio requirement for a particular excavation. This can usually be determined through visual observation. Permanent spoil can change undisturbed soil to disturbed soil and dramatically alter slope requirements.
  1926.651(j)
  Protection of employees from loose rock or soil
  1926.651(j)(1)
  Adequate protection shall be provided to protect employees from loose rock or soil that could pose a hazard by falling or rolling from an excavation face. Such protection shall consist of scaling to remove loose material; installation of protective barricades at intervals as necessary on the face to stop and contain falling material; or other means that provide equivalent protection.
  1926.651(j)(2)
  Employees shall be protected from excavated or other materials or equipment that could pose a hazard by falling or rolling into excavations. Protection shall be provided by placing and keeping such materials or equipment at least 2 feet (.61 m) from the edge of excavations, or by the use of retaining devices that are sufficient to prevent materials or equipment from falling or rolling into excavations, or by a combination of both if necessary.
In these photos you can see that the spoil pile was not placed 2 feet away from edge of the excavation which now adds height of the pile to the depth of the trench.
These photos depict violations of 1926.651 involving protection of employees from loose rock and soil, access and egress as well as the competent person performing his/her duties.

## Slide 16
Loose Rock and Soil Protection
Hazards
Notes: As the illustration shows Spoil Pile am Material Storage must be at least 2 ft away from the edge.

## Slide 17
Loose Rock and Soil Protection
Hazards
Notes: If is not possible to move loose material from the edge then some type of protective barrier must be installed to prevent material from entering the trench or excavation.

## Slide 18
Ingress and Egress
Hazards
Notes: Ingress and egress.
Access to and exit from the trench require the following conditions:
Trenches 4 feet or more in depth should be provided with a fixed means of egress.
Spacing between ladders or other means of egress must be such that a worker will not have to travel more than 25 feet laterally to the nearest means of egress.
Ladders must be secured and extend a minimum of 36 inches (0.9 meters) above the landing.
Metal ladders should be used with caution, particularly when electric utilities are present.

## Slide 19
Access to and exit from the trench require the following conditions:
    Trenches 4 ft or more in depth should be provided with a fixed means of egress.
    Spacing between ladders or other means of egress must be such that a worker will not have to travel more than 25 ft laterally to the nearest means of egress.
    Ladders must be secured and extend a minimum of 36 in (0.9 m) above the landing.
    Metal ladders should be used with caution, particularly when electric utilities are present.
Ingress and Egress
Hazards
Notes: 1926.651(c)
Access and egress -
1926.651(c)(1)
Structural ramps.
1926.651(c)(1)(i)
Structural ramps that are used solely by employees as a means of access or egress from excavations shall be designed by a competent person. Structural ramps used for access or egress of equipment shall be designed by a competent person qualified in structural design, and shall be constructed in accordance with the design.
1926.651(c)(1)(ii)
Ramps and runways constructed of two or more structural members shall have the structural members connected together to prevent displacement.
1926.651(c)(1)(iii)
Structural members used for ramps and runways shall be of uniform thickness.
1926.651(c)(1)(iv)
Cleats or other appropriate means used to connect runway structural members shall be attached to the bottom of the runway or shall be attached in a manner to prevent tripping.
1926.651(c)(1)(v)
Structural ramps used in lieu of steps shall be provided with cleats or other surface treatments on the top surface to prevent slipping.
1926.651(c)(2)
Means of egress from trench excavations. A stairway, ladder, ramp or other safe means of egress shall be located in trench excavations that are 4 feet (1.22 m) or more in depth so as to require no more than 25 feet (7.62 m) of lateral travel for employees.

## Slide 20
Ingress and Egress
Hazards
Notes: Trenches 4 feet or more in depth should be provided with a fixed means of egress.
Spacing between ladders or other means of egress must be such that a worker will not have to travel more than 25 feet laterally to the nearest means of egress.

## Slide 21
Ingress and Egress
Hazards
Notes: Manufactured/Engineered systems are the best to use in most situations. Avoid just using what is just left around the project that may not be the best fit.

## Slide 22
Ingress and Egress
Hazards
Notes: Good examples use of proper access

## Slide 23
Exposure to Vehicles
Hazards
Notes: Any large, heavy movement near an excavation results in vibration of the surrounding soils. This movement can result in soil failure. Moving machinery, nearby traffic, pile driving and blasting all cause vibration in surrounding soils.
Vibration-related soil failures can occur in all types of soil. However, certain types of soils are more susceptible to vibration failures than others. For example, sandy soils tolerate less vibration than clay soils.
Since actual soil conditions may be a mixture of more than one soil type, it is better to play it safe when planning the slope of an excavation

## Slide 24
Exposure to Vehicles
Hazards
Notes: Without proper traffic control there is always the chance a member of the general public and their vehicle can enter the work area and create a dangerous situation. These hazards are expected of all projects that are adjacent on roadways.

## Slide 25
Procedures to protect employees from being injured or killed by vehicle traffic include:
    Providing employees with and requiring them to wear warning vests or other suitable garments marked with or made of reflectorized or high-visibility materials.
    Requiring a designated, trained flag person along with signs, signals, and barricades when necessary.
Exposure to Vehicles
Hazards
Notes: Procedures to protect employees from being injured or killed by vehicle traffic include:
Providing employees with and requiring them to wear warning vests or other suitable garments marked with or made of reflectorized or high-visibility materials.
Requiring a designated, trained flag person along with signs, signals, and barricades when necessary.
1926.651(d)
Exposure to vehicular traffic. Employees exposed to public vehicular traffic shall be provided with, and shall wear, warning vests or other suitable garments marked with or made of reflectorized or high-visibility material.

## Slide 26
Exposure to Vehicles
Hazards
Notes: Employees exposed to public vehicular traffic shall be provided with, and shall wear, warning vests or other suitable garments marked with or made of reflectorized or high-visibility material.
The photos depict good work zone set up.

## Slide 27
Warning Systems for Mobile Equipment
Hazards
Notes: Warning systems for mobile equipment. The following steps should be taken to prevent vehicles from accidentally falling into the trench:
Barricades must be installed where necessary. Hand or mechanical signals must be used as required.
Stop logs must be installed if there is a danger of vehicles falling into the trench.
Soil should be graded away from the excavation; this will assist in vehicle control and channeling of run-off water.

## Slide 28
Warning Systems for Mobile Equipment
Hazards
Notes: Warning systems for mobile equipment. The following steps should be taken to prevent vehicles from accidentally falling into the trench:
Barricades must be installed where necessary. Hand or mechanical signals must be used as required.
Stop logs must be installed if there is a danger of vehicles falling into the trench.
Soil should be graded away from the excavation; this will assist in vehicle control and channeling of run-off water.

## Slide 29
The following steps should be taken to prevent vehicles from accidentally falling into the trench:
    Barricades must be installed where necessary.
    Hand or mechanical signals must be used as required.
    Stop logs must be installed if there is a danger of vehicles falling into the trench.
    Soil should be graded away from the excavation; this will assist in vehicle control and channeling of run-off water
Warning Systems for Mobile Equipment
Hazards
Notes: 1926.651(f)
Warning system for mobile equipment. When mobile equipment is operated adjacent to an excavation, or when such equipment is required to approach the edge of an excavation, and the operator does not have a clear and direct view of the edge of the excavation, a warning system shall be utilized such as barricades, hand or mechanical signals, or stop logs. If possible, the grade should be away from the excavation.

## Slide 30
Warning Systems for Mobile Equipment
Hazards
Notes: This photo show the need for some type of warning system, so the equipment does not get to close to the protected excavation. Using a stop log, fencing, or waring tape could be used if it does not impair the vision of the operator.

## Slide 31
Warning Systems for Mobile Equipment
Hazards
Notes: The following steps should be taken to prevent vehicles from accidentally falling into the trench:
Barricades must be installed where necessary.
Hand or mechanical signals must be used as required.
Stop logs must be installed if there is a danger of vehicles falling into the trench.
Soil should be graded away from the excavation; this will assist in vehicle control and channeling of run-off water.

## Slide 32
Warning Systems for Mobile Equipment
Hazards
Notes: Making sure that you always look for ways to protect people from equipment.

## Slide 33
Warning Systems for Mobile Equipment
Hazards

## Slide 34
Exposure to Falling Loads
Hazards
Notes: Employees must be protected from loads or objects falling from lifting or digging equipment. Procedures designed to ensure their protection include:
Employees are not permitted to work under raised loads.
Employees are required to stand away from equipment that is being loaded or unloaded.
Equipment operators or truck drivers may stay in their equipment during loading and unloading if the equipment is properly equipped with a cab shield or adequate canopy.
1926.651(e)
Exposure to falling loads. No employee shall be permitted underneath loads handled by lifting or digging equipment. Employees shall be required to stand away from any vehicle being loaded or unloaded to avoid being struck by any spillage or falling materials. Operators may remain in the cabs of vehicles being loaded or unloaded when the vehicles are equipped, in accordance with §1926.601(b)(6), to provide adequate protection for the operator during loading and unloading operations

## Slide 35
Exposure to Falling Loads
Hazards
Notes: Backfilled areas may have lower bearing capacities.
Do not set up on backfilled areas unless backfill is properly compacted and larger mats or floats are used

## Slide 36
Employees must be protected from loads or objects falling from lifting or digging equipment.
Procedures designed to ensure their protection include:
    Employees are not permitted to work under raised loads.
    Employees are required to stand away from equipment that is being loaded or unloaded.
    Equipment operators or truck drivers may stay in their equipment during loading and unloading if the equipment is properly equipped with a cab shield or adequate canopy.
Exposure to Falling Loads
Hazards

## Slide 37
Exposure to Falling Loads
Hazards
Notes: Exposure to falling loads. Employees must be protected from loads or objects falling from lifting or digging equipment. Procedures designed to ensure their protection include:
Employees are not permitted to work under raised loads. Employees are required to stand away from equipment that is being loaded or unloaded. Equipment operators or truck drivers may stay in their equipment during loading and unloading if the equipment is properly equipped with a cab shield or adequate canopy

## Slide 38
Exposure to Falling Loads
Hazards
Notes: Taglines should be used so you do not have put yourself under the load

## Slide 39
Hazardous Atmospheres and Confined Spaces
Hazards
Notes: Both photos depict possible sources of hazardous atmospheres that can create conditions to classify some excavations confined spaces.
The photo on the right show that crew operations can create hazardous atmospheres that should have been anticipated. The photo on the left is a different situation where the now open pipe can be a source of hazardous atmospheres. With the possibility of both sources present on the project a gas meter specifically designed for what you may encounter should be on the project in use.

## Slide 40
Employees shall not be permitted to work in hazardous and/or toxic atmospheres. Such atmospheres include those with:
    Less than 19.5% or more than 23.5% oxygen;
    A combustible gas concentration greater than 20% of the lower flammable limit
  All operations involving such atmospheres must be conducted in accordance with OSHA requirements
Hazardous Atmospheres and Confined Spaces
Hazards
Notes: 1926.651(g)
Hazardous atmospheres -
1926.651(g)(1)
Testing and controls. In addition to the requirements set forth in subparts D and E of this part (29 CFR 1926.50 - 1926.107) to prevent exposure to harmful levels of atmospheric contaminants and to assure acceptable atmospheric conditions, the following requirements shall apply:
1926.651(g)(1)(i)
Where oxygen deficiency (atmospheres containing less than 19.5 percent oxygen) or a hazardous atmosphere exists or could reasonably be expected to exist, such as in excavations in landfill areas or excavations in areas where hazardous substances are stored nearby, the atmospheres in the excavation shall be tested before employees enter excavations greater than 4 feet (1.22 m) in depth.
1926.651(g)(1)(ii)
Adequate precautions shall be taken to prevent employee exposure to atmospheres containing less than 19.5 percent oxygen and other hazardous atmospheres. These precautions include providing proper respiratory protection or ventilation in accordance with subparts D and E of this part respectively.
1926.651(g)(1)(iii)
Adequate precaution shall be taken such as providing ventilation, to prevent employee exposure to an atmosphere containing a concentration of a flammable gas in excess of 20 percent of the lower flammable limit of the gas.
1926.651(g)(1)(iv)
When controls are used that are intended to reduce the level of atmospheric contaminants to acceptable levels, testing shall be conducted as often as necessary to ensure that the atmosphere remains safe.
1926.651(g)(2)
Emergency rescue equipment.
1926.651(g)(2)(i)
Emergency rescue equipment, such as breathing apparatus, a safety harness and line, or a basket stretcher, shall be readily available where hazardous atmospheric conditions exist or may reasonably be expected to develop during work in an excavation. This equipment shall be attended when in use.

## Slide 41
When testing for atmospheric contaminants, the following should be considered:
    Testing should be conducted before employees enter the trench and should be done regularly to ensure that the trench remains safe.
    The frequency of testing should be increased if equipment is operating in the trench.
    Testing frequency should also be increased if welding, cutting, or burning is done in the trench.
Hazardous Atmospheres and Confined Spaces
Hazards
Notes: All operations involving such atmospheres must be conducted in accordance with OSHA requirements for occupational health and environmental controls (see 29 CFR Part 1926 Subpart D) for personal protective equipment and for lifesaving equipment (see 29 CFR Part 1926 Subpart E). Engineering controls (e.g., ventilation) and respiratory protection may be required.

## Slide 42
Hazardous Atmospheres and Confined Spaces
Hazards
Notes: When testing for atmospheric contaminants, the following should be considered:
Testing should be conducted before employees enter the trench and should be done regularly to ensure that the trench remains safe.
The frequency of testing should be increased if equipment is operating in the trench.
Testing frequency should also be increased if welding, cutting, or burning is done in the trench
Employees required to wear respiratory protection must be trained, fit-tested, and enrolled in a respiratory protection program. Some trenches qualify as confined spaces. When this occurs, compliance with the Confined Space Standard is also required.

## Slide 43
Standing Water and Water Accumulation
Hazards
Notes: Methods for controlling standing water and water accumulation must be provided and should consist of the following if employees are permitted to work in the excavation:
Use of special support or shield systems approved by a registered professional engineer.
Water removal equipment, i.e. well pointing, used and monitored by a competent person.
Safety harnesses and lifelines used in conformance with 29 CFR 1926.104.
Surface water diverted away from the trench.
Employees removed from the trench during rainstorms.
Trenches carefully inspected by a competent person after each rain and before employees are permitted to re-enter the trench.

## Slide 44
Methods for controlling standing water and water accumulation must be provided and should consist of the following if employees are permitted to work in the excavation:
    Use of special support or shield systems approved by a registered professional engineer.
    Water removal equipment, i.e. well pointing, used and monitored by a competent person.
    Safety harnesses and lifelines used in conformance with 29 CFR 1926.104.
Standing Water and Water Accumulation
Hazards
Notes: 1926.651(h)
Protection from hazards associated with water accumulation.
1926.651(h)(1)
Employees shall not work in excavations in which there is accumulated water, or in excavations in which water is accumulating, unless adequate precautions have been taken to protect employees against the hazards posed by water accumulation. The precautions necessary to protect employees adequately vary with each situation, but could include special support or shield systems to protect from cave-ins, water removal to control the level of accumulating water, or use of a safety harness and lifeline.
1926.651(h)(2)
If water is controlled or prevented from accumulating by the use of water removal equipment, the water removal equipment and operations shall be monitored by a competent person to ensure proper operation.
1926.651(h)(3)
If excavation work interrupts the natural drainage of surface water (such as streams), diversion ditches, dikes, or other suitable means shall be used to prevent surface water from entering the excavation and to provide adequate drainage of the area adjacent to the excavation. Excavations subject to runoff from heavy rains will require an inspection by a competent person and compliance with paragraphs (h)(1) and (h)(2) of this section.

## Slide 45
Methods for controlling standing water and water accumulation must be provided and should consist of the following if employees are permitted to work in the excavation (Con’t) :
    Surface water diverted away from the trench.
    Employees removed from the trench during rainstorms.
    Trenches carefully inspected by a competent person after each rain and before employees are permitted to re-enter the trench.
Standing Water and Water Accumulation
Hazards
Notes: 1926.651(h)
Protection from hazards associated with water accumulation.
1926.651(h)(1)
Employees shall not work in excavations in which there is accumulated water, or in excavations in which water is accumulating, unless adequate precautions have been taken to protect employees against the hazards posed by water accumulation. The precautions necessary to protect employees adequately vary with each situation, but could include special support or shield systems to protect from cave-ins, water removal to control the level of accumulating water, or use of a safety harness and lifeline.
1926.651(h)(2)
If water is controlled or prevented from accumulating by the use of water removal equipment, the water removal equipment and operations shall be monitored by a competent person to ensure proper operation.
1926.651(h)(3)
If excavation work interrupts the natural drainage of surface water (such as streams), diversion ditches, dikes, or other suitable means shall be used to prevent surface water from entering the excavation and to provide adequate drainage of the area adjacent to the excavation. Excavations subject to runoff from heavy rains will require an inspection by a competent person and compliance with paragraphs (h)(1) and (h)(2) of this section.

## Slide 46
Standing Water and Water Accumulation
Hazards
Notes: A system has to be in place to control water accumulation such as dewatering pumps, sumps or some other type of drainage system.

## Slide 47
Questions?
Hazards