## Slide 1
Soil Testing and Classification
Oct. 2021 – Sep. 2022
Trenching & Excavation Hazards in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
This session describes a method of classifying soil and rock deposits based on site and environmental conditions, and on the structure and composition of the earth deposits.
Proper sloping or benching systems designed in accordance with the requirements.
Use of shoring systems including timber shoring, aluminum hydraulic shoring, sheet piling, or other engineered protection systems.
Learning Objectives
Soil Testing & Classification
Notes: This appendix applies when a sloping or benching system is designed in accordance with the requirements set forth in § 1926.652(b)(2) as a method of protection for employees from cave-ins. This appendix also applies when timber shoring for excavations is designed as a method of protection from cave-ins in accordance with appendix C to subpart P of part 1926, and when aluminum hydraulic shoring is designed in accordance with appendix D. This appendix also applies if other protective systems are designed and selected for use from data prepared in accordance with the requirements set forth in § 1926.652(c), and the use of the data is predicated on the use of the soil classification system set forth in this appendix.

## Slide 3
An inspection shall be conducted by the competent person prior to the start of work and as needed throughout the shift.
Inspections shall also be made after every rainstorm or other hazard increasing occurrence. These inspections are only required when employee exposure can be reasonably anticipated.
Competent Person
Soil Testing & Classification
Notes: 1926.651(k)(1)
Daily inspections of excavations, the adjacent areas, and protective systems shall be made by a competent person for evidence of a situation that could result in possible cave-ins, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions. An inspection shall be conducted by the competent person prior to the start of work and as needed throughout the shift. Inspections shall also be made after every rainstorm or other hazard increasing occurrence. These inspections are only required when employee exposure can be reasonably anticipated.
1926.651(k)(2)
Where the competent person finds evidence of a situation that could result in a possible cave-in, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions, exposed employees shall be removed from the hazardous area until the necessary precautions have been taken to ensure their safety.

## Slide 4
Daily inspections of excavations, the adjacent areas, and protective systems shall be made by a competent person for:
    evidence of a situation that could result in possible cave-ins,
    indications of failure of protective systems,
    hazardous atmospheres,
    or other hazardous conditions.
Competent Person
Soil Testing & Classification
Notes: 1926.651(k)(1)
Daily inspections of excavations, the adjacent areas, and protective systems shall be made by a competent person for evidence of a situation that could result in possible cave-ins, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions. An inspection shall be conducted by the competent person prior to the start of work and as needed throughout the shift. Inspections shall also be made after every rainstorm or other hazard increasing occurrence. These inspections are only required when employee exposure can be reasonably anticipated.
1926.651(k)(2)
Where the competent person finds evidence of a situation that could result in a possible cave-in, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions, exposed employees shall be removed from the hazardous area until the necessary precautions have been taken to ensure their safety.

## Slide 5
Pre-inspect the job site
Determine soil condition and type
Determine protection systems
Assure proper access & egress
Monitor environmental conditions
Inspect & provide employee safety
Duties of a Competent Person
Soil Testing & Classification

## Slide 6
Each soil and rock deposit shall be classified by a competent person as Stable Rock, Type A, Type B, or Type C
The classification of the deposits shall be made based on the results of at least one visual and at least one manual analysis.
Such analyses shall be conducted by a competent person
The visual and manual analyses, shall be conducted to provide sufficient quantities to get a good understanding of the soil types.
Soil Testing by a Competent Person
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification
(c) Requirements-
(1) Classification of soil and rock deposits. Each soil and rock deposit shall be classified by a competent person as Stable Rock, Type A, Type B, or Type C in accordance with the definitions set forth in paragraph (b) of this appendix.
(2) Basis of classification. The classification of the deposits shall be made based on the results of at least one visual and at least one manual analysis. Such analyses shall be conducted by a competent person using tests described in paragraph (d) below, or in other recognized methods of soil classification and testing such as those adopted by the America Society for Testing Materials, or the U.S. Department of Agriculture textural classification system.
(3) Visual and manual analyses. The visual and manual analyses, such as those noted as being acceptable in paragraph (d) of this appendix, shall be designed and conducted to provide sufficient quantitative and qualitative information as may be necessary to identify properly the properties, factors, and conditions affecting the classification of the deposits.
(4) Layered systems. In a layered system, the system shall be classified in accordance with its weakest layer. However, each layer may be classified individually where a more stable layer lies under a less stable layer.
(5) Reclassification. If, after classifying a deposit, the properties, factors, or conditions affecting its classification change in any way, the changes shall be evaluated by a competent person. The deposit shall be reclassified as necessary to reflect the changed circumstances.

## Slide 7
A method of categorizing soil and rock deposits in a hierarchy of Stable Rock,
Type A, Type B, and Type C, in decreasing order of stability.
The categories are determined based on an analysis of the properties and performance characteristics of the deposits and the environmental conditions of exposure.
Soil Classification
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification - Definitions

## Slide 8
Documentation is NOT Required.
But having a document or a trenching log or checklist is a BEST PRACTICE
Documentation of Testing
Soil Testing & Classification
Notes: 1. 1926 Subpart P App A - Soil Classification
(a) Scope and application-
(1) Scope. This appendix describes a method of classifying soil and rock deposits based on site and environmental conditions, and on the structure and composition of the earth deposits. The appendix contains definitions, sets forth requirements, and describes acceptable visual and manual tests for use in classifying soils.
(2) Application. This appendix applies when a sloping or benching system is designed in accordance with the requirements set forth in § 1926.652(b)(2) as a method of protection for employees from cave-ins. This appendix also applies when timber shoring for excavations is designed as a method of protection from cave-ins in accordance with appendix C to subpart P of part 1926, and when aluminum hydraulic shoring is designed in accordance with appendix D. This appendix also applies if other protective systems are designed and selected for use from data prepared in accordance with the requirements set forth in § 1926.652(c), and the use of the data is predicated on the use of the soil classification system set forth in this appendix.

## Slide 9
Clay (fine grained soil), or soil with a high clay content, which has cohesive strength.
Cohesive soil does not crumble, can be excavated with vertical side slopes, and is plastic when moist.
Cohesive soil is hard to break up when dry and exhibits significant cohesion when submerged.
Cohesive soils include clayey silt, sandy clay, silty clay, clay and organic clay.
Cohesive soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification - Definitions

## Slide 10
Gravel, sand, or silt, (coarse grained soil) with little or no clay content.
Granular soil has no cohesive strength. Some moist granular soils exhibit apparent cohesion.
Granular soil cannot be molded when moist and crumbles easily when dry.
Granular soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification - Definitions

## Slide 11
Visual analysis is conducted to determine qualitative information regarding the excavation site in general,
the soil adjacent to the excavation,
the soil forming the sides of the open excavation,
and the soil taken as samples from excavated material.
Visual Tests
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification Definitions
(1) Visual tests. Visual analysis is conducted to determine qualitative information regarding the excavation site in general, the soil adjacent to the excavation, the soil forming the sides of the open excavation, and the soil taken as samples from excavated material.
(i) Observe samples of soil that are excavated and soil in the sides of the excavation. Estimate the range of particle sizes and the relative amounts of the particle sizes. Soil that is primarily composed of fine-grained material is cohesive material. Soil composed primarily of coarse-grained sand or gravel is granular material.
(ii) Observe soil as it is excavated. Soil that remains in clumps when excavated is cohesive. Soil that breaks up easily and does not stay in clumps is granular.
(iii) Observe the side of the opened excavation and the surface area adjacent to the excavation. Crack-like openings such as tension cracks could indicate fissured material. If chunks of soil spall off a vertical side, the soil could be fissured. Small spalls are evidence of moving ground and are indications of potentially hazardous situations.
(iv) Observe the area adjacent to the excavation and the excavation itself for evidence of existing utility and other underground structures, and to identify previously disturbed soil.
(v) Observe the opened side of the excavation to identify layered systems. Examine layered systems to identify if the layers slope toward the excavation. Estimate the degree of slope of the layers.
(vi) Observe the area adjacent to the excavation and the sides of the opened excavation for evidence of surface water, water seeping from the sides of the excavation, or the location of the level of the water table.
(vii) Observe the area adjacent to the excavation and the area within the excavation for sources of vibration that may affect the stability of the excavation face.

## Slide 12
Comes out of bucket in large clumps – Cohesive.
Spoil pile flows freely - Granular.
Excavation face stands after bucket removed – Cohesive.
Look for seeping water – Downgrade Type
Look for fissures in soil face – Downgrade type
Visual Tests
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification
(1) Visual tests. Visual analysis is conducted to determine qualitative information regarding the excavation site in general, the soil adjacent to the excavation, the soil forming the sides of the open excavation, and the soil taken as samples from excavated material.
(i) Observe samples of soil that are excavated and soil in the sides of the excavation. Estimate the range of particle sizes and the relative amounts of the particle sizes. Soil that is primarily composed of fine-grained material is cohesive material. Soil composed primarily of coarse-grained sand or gravel is granular material.
(ii) Observe soil as it is excavated. Soil that remains in clumps when excavated is cohesive. Soil that breaks up easily and does not stay in clumps is granular.
(iii) Observe the side of the opened excavation and the surface area adjacent to the excavation. Crack-like openings such as tension cracks could indicate fissured material. If chunks of soil spall off a vertical side, the soil could be fissured. Small spalls are evidence of moving ground and are indications of potentially hazardous situations.
(iv) Observe the area adjacent to the excavation and the excavation itself for evidence of existing utility and other underground structures, and to identify previously disturbed soil.
(v) Observe the opened side of the excavation to identify layered systems. Examine layered systems to identify if the layers slope toward the excavation. Estimate the degree of slope of the layers.
(vi) Observe the area adjacent to the excavation and the sides of the opened excavation for evidence of surface water, water seeping from the sides of the excavation, or the location of the level of the water table.
(vii) Observe the area adjacent to the excavation and the area within the excavation for sources of vibration that may affect the stability of the excavation face.

## Slide 13
Strong cohesive soils
Stiff clays
Cohesive sands & gravels.
No fissures or cracks.
Not saturated.
Unconfined Compressive Strength of >1.5 tons per sq. ft.
Type A Soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification Definitions
Type A means cohesive soils with an unconfined compressive strength of 1.5 ton per square foot (tsf) (144 kPa) or greater. Examples of cohesive soils are: clay, silty clay, sandy clay, clay loam and, in some cases, silty clay loam and sandy clay loam. Cemented soils such as caliche and hardpan are also considered Type A. However, no soil is Type A if:
(i) The soil is fissured; or
(ii) The soil is subject to vibration from heavy traffic, pile driving, or similar effects; or
(iii) The soil has been previously disturbed; or
(iv) The soil is part of a sloped, layered system where the layers dip into the excavation on a slope of four horizontal to one vertical (4H:1V) or greater; or
(v) The material is subject to other factors that would require it to be classified as a less stable material.

## Slide 14
Weak cohesive soils.
Medium stiff clays.
Fractured or unstable rock.
Clayey sands or clayey silt.
May have fissures or cracks.
Type B Soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification Definitions
Type B means:
(i) Cohesive soil with an unconfined compressive strength greater than 0.5 tsf (48 kPa) but less than 1.5 tsf (144 kPa); or
(ii) Granular cohesionless soils including: angular gravel (similar to crushed rock), silt, silt loam, sandy loam and, in some cases, silty clay loam and sandy clay loam.
(iii) Previously disturbed soils except those which would otherwise be classified as Type C soil.
(iv) Soil that meets the unconfined compressive strength or cementation requirements for Type A, but is fissured or subject to vibration; or

## Slide 15
Not saturated.
Unconfined Compressive Strength of 0.5 – 1.5 tons per sq. ft.
Type B Soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification Definitions
Type B means:
(i) Cohesive soil with an unconfined compressive strength greater than 0.5 tsf (48 kPa) but less than 1.5 tsf (144 kPa); or
(ii) Granular cohesionless soils including: angular gravel (similar to crushed rock), silt, silt loam, sandy loam and, in some cases, silty clay loam and sandy clay loam.
(iii) Previously disturbed soils except those which would otherwise be classified as Type C soil.
(iv) Soil that meets the unconfined compressive strength or cementation requirements for Type A, but is fissured or subject to vibration; or

## Slide 16
Cohesionless sands
Cohesionless fills
Gravel
Silty granular soils
May be saturated
Unconfined Compressive Strength of <.5 tons per sq. ft.
Type C Soil
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification Definitions
Type C means:
(i) Cohesive soil with an unconfined compressive strength of 0.5 tsf (48 kPa) or less; or
(ii) Granular soils including gravel, sand, and loamy sand; or
(iii) Submerged soil or soil from which water is freely seeping; or
(iv) Submerged rock that is not stable; or
(v) Material in a sloped, layered system where the layers dip into the excavation on a slope of four horizontal to one vertical (4H:1V) or steeper.

## Slide 17
Natural solid mineral (Rock) matter that can be excavated with vertical sides and remain intact while exposed
Stable Rock
Soil Testing & Classification

## Slide 18
OSHA Soil Test Video
Soil Testing & Classification

## Slide 19
Manual analysis of soil samples is conducted to determine quantitative as well as qualitative properties of soil and to provide more information in order to classify soil properly.
Thumb Penetration Test
Penetrometer Test
Thread Plasticity Test
Ball Sample Test
Dry Sample Test
Water Sedimentation Test
Manual Tests
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification
(2) Manual tests. Manual analysis of soil samples is conducted to determine quantitative as well as qualitative properties of soil and to provide more information in order to classify soil properly.
(i) Plasticity. Mold a moist or wet sample of soil into a ball and attempt to roll it into threads as thin as 1⁄8-inch in diameter. Cohesive material can be successfully rolled into threads without crumbling. For example, if at least a two inch (50 mm) length of 1⁄8- inch thread can be held on one end without tearing, the soil is cohesive.
(ii) Dry strength. If the soil is dry and crumbles on its own or with moderate pressure into individual grains or fine powder, it is granular (any combination of gravel, sand, or silt). If the soil is dry and falls into clumps which break up into smaller clumps, but the smaller clumps can only be broken up with difficulty, it may be clay in any combination with gravel, sand or silt. If the dry soil breaks into clumps which do not break up into small clumps and which can only be broken with difficulty, and there is no visual indication the soil is fissured, the soil may be considered unfissured.
(iii) Thumb penetration. The thumb penetration test can be used to estimate the unconfined compressive strength of cohesive soils. (This test is based on the thumb penetration test described in American Society for Testing and Materials (ASTM) Standard designation D2488—‘‘Standard Recommended Practice for Description of Soils (Visual—Manual Procedure).’’) Type A soils with an unconfined compressive strength of 1.5 tsf can be readily indented by the thumb; however, they can be penetrated by the thumb only with very great effort. Type C soils with an unconfined compressive strength of 0.5 tsf can be easily penetrated several inches by the thumb, and can be molded by light finger pressure. This test should be conducted on an undisturbed soil sample, such as a large clump of spoil, as soon as practicable after excavation to keep to a minimum the effects of exposure to drying influences. If the excavation is later exposed to wetting influences (rain, flooding), the classification of the soil must be changed accordingly.
(iv) Other strength tests. Estimates of unconfined compressive strength of soils can also be obtained by use of a pocket penetrometer or by using a hand-operated shear vane.
(v) Drying test. The basic purpose of the drying test is to differentiate between cohesive material with fissures, unfissured cohesive material, and granular material. The procedure for the drying test involves drying a sample of soil that is approximately one inch thick (2.54 cm) and six inches (15.24 cm) in diameter until it is thoroughly dry:
(A) If the sample develops cracks as it dries, significant fissures are indicated.
(B) Samples that dry without cracking are to be broken by hand. If considerable force is necessary to break a sample, the soil has significant cohesive material content. The soil can be classified as an unfissured cohesive material and the unconfined compressive strength should be determined.
(C) If a sample breaks easily by hand, it is either a fissured cohesive material or a granular material. To distinguish between the two, pulverize the dried clumps of the sample by hand or by stepping on them. If the clumps do not pulverize easily, the material is cohesive with fissures. If they pulverize easily into very small fragments, the material is granular

## Slide 20
Thumb Penetration Test
See how far you can penetrate your thumb into a large clump.
Type “A” - ½ thumbnail
Type “B” - Full thumbnail
Type “C” – To knuckle
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification
(d)(2)(iii) Thumb penetration. The thumb penetration test can be used to estimate the unconfined compressive strength of cohesive soils. (This test is based on the thumb penetration test described in American Society for Testing and Materials (ASTM) Standard designation D2488—‘‘Standard Recommended Practice for Description of Soils (Visual—Manual Procedure).’’) Type A soils with an unconfined compressive strength of 1.5 tsf can be readily indented by the thumb; however, they can be penetrated by the thumb only with very great effort. Type C soils with an unconfined compressive strength of 0.5 tsf can be easily penetrated several inches by the thumb, and can be molded by light finger pressure. This test should be conducted on an undisturbed soil sample, such as a large clump of spoil, as soon as practicable after excavation to keep to a minimum the effects of exposure to drying influences. If the excavation is later exposed to wetting influences (rain, flooding), the classification of the soil must be changed accordingly.

## Slide 21
Pocket Penetrometer
(Cohesive Soils Only)
Insert the penetrometer into the soil sample up to marker ring.
Read the unconfined compressive strength at the bottom of the red slip ring.
Soil Testing & Classification

## Slide 22
Plasticity Thread Test
Roll soil into a 1/8” diameter thread.
Hold vertically from one end.
If you can hold a thread of more than 2”, the soil is cohesive.
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification
(d)(2)(i) Plasticity. Mold a moist or wet sample of soil into a ball and attempt to roll it into threads as thin as 1⁄8-inch in diameter. Cohesive material can be successfully rolled into threads without crumbling. For example, if at least a two inch (50 mm) length of 1⁄8- inch thread can be held on one end without tearing, the soil is cohesive.

## Slide 23
Ball Sample Test
Roll a wet sample of soil into a ball.
If the ball is firm and stable the soil is cohesive.
If the ball falls apart with handling, the soil is granular.
Soil Testing & Classification

## Slide 24
Dry Sample Test
Strong Cohesive - A large dry sample breaks up only with force.
Weak Cohesive - A large sample breaks easily into smaller clumps you cannot crush.
Granular - Clumps crush easily into particles.
Soil Testing & Classification
Notes: 1926 Subpart P App A - Soil Classification - Dry strength. If the soil is dry and crumbles on its own or with moderate pressure into individual grains or fine powder, it is granular (any combination of gravel, sand, or silt). If the soil is dry and falls into clumps which break up into smaller clumps, but the smaller clumps can only be broken up with difficulty, it may be clay in any combination with gravel, sand or silt. If the dry soil breaks into clumps which do not break up into small clumps and which can only be broken with difficulty, and there is no visual indication the soil is fissured, the soil may be considered unfissured.
(d)(2)(v) Drying test. The basic purpose of the drying test is to differentiate between cohesive material with fissures, unfissured cohesive material, and granular material. The procedure for the drying test involves drying a sample of soil that is approximately one inch thick (2.54 cm) and six inches (15.24 cm) in diameter until it is thoroughly dry:
(A) If the sample develops cracks as it dries, significant fissures are indicated.
(B) Samples that dry without cracking are to be broken by hand. If considerable force is necessary to break a sample, the soil has significant cohesive material content. The soil can be classified as an unfissured cohesive material and the unconfined compressive strength should be determined.
(C) If a sample breaks easily by hand, it is either a fissured cohesive material or a granular material. To distinguish between the two, pulverize the dried clumps of the sample by hand or by stepping on them. If the clumps do not pulverize easily, the material is cohesive with fissures. If they pulverize easily into very small fragments, the material is granular

## Slide 25
Remove all rocks or large particles.
Place soil on a glass jar full of water.
Shake until all particles are suspended.
Silt will settle in about 60 seconds.
Clay may take an hour.
Estimate percentage of Clay, Silt and Sand
Water Sedimentation Test
Soil Testing & Classification

## Slide 26
Check soil percentages on chart
Textural Classification Chart
COHESIVE
GRANULAR
Soil Testing & Classification

## Slide 27
Once the soil is classified the competent person can then establish the protection systems required to keep the employees safe in the excavation.
Appendix B of OSHA Subpart P describes the sloping methods.
Appendix E of OSHA Subpart P describes various shoring methods.
Soil Protection Based on Classification
Soil Testing & Classification

## Slide 28
Questions?
Soil Testing & Classification